## Slide 1: Transfemoral prosthesis

## Slide 3
Amputation b/w femoral epicondyles and greater trochanter are fitted with transfemoral prosthesis.
Consist of
(1) foot-ankle assembly
(2) shank
(3)knee unit
(4)socket
(5)Suspension device

## Slide 4: (1) foot-ankle assembly
SACH Foot is most commonly used
Single-axis foot is somewhat more frequently prescribed . Nevertheless, any foot, including the energy storing/releasing designs can be incorporated in a transfemoral prosthesis.

## Slide 5: Shank
Either the sturdy exoskeletal or endoskeletal shank may be used.
Endoskeletal shank creates a more pleasing appearance , particularly in the knee area and adjustable , and lighter than exo…

## Slide 6: Knee unit
Prosthetic knee enables the user to bend the knee when sitting or kneeling.
Commercial knee units may be described according to four features.
1)axis
2) friction mechanism
3) extension aid
4) mechanical stabilizer
Many combinations of features are available; not every knee unit has all four components.

## Slide 7: (a)

## Slide 8: Axis system
The thigh piece can be connected to the shank either by a simple single-axis hinge or by polycentric linkage.
Polycentric systems have four or more pivoting bars and provide greater stability to the knee. This style is less common b/c of its greater complexity.

## Slide 9: (b)Friction Mechanism
If the knee does not have sufficient friction to retard its natural pendular action
Friction mechanisms change the knee swing by modifying the speed of the knee motion during various parts of the swing phase and by affecting knee swing according to walking speed.

## Slide 10
Constant and variable:-
The most popular knee unit has constant friction
Variable friction:-
In which the amount of friction changes during a given swing phase
At early swing:-high friction…..retard excessive knee flexion
During mid swing:- friction diminishes to permit the knee swing easily
Late swing:- friction increases to dampen impact

## Slide 11: (c) Extension aid
Assist knee extension
Simplest type…. External aid consisting of elastic webbing in front of knee axis.
Int ext aid ….. Elastic strap or coiled ring within the knee unit…. Functions identically to the ext aid during walking

## Slide 12: d) Stabilizers
Most knee units donot have a special device to increase stability. The patient controls knee action by hip motion, aided by the alignment of the knee in relation to other components of the prosthesis.
Elderly or debilitating pt may benefit from stabilizing mechanism
a) manual lock ….. Simplest mechanical stabilizer
b)friction brake…… more elaborate stbilizing system, provides very high friction mechanism during early stance, resisting any tendency of the knee to flex.

## Slide 13: socket
As with all prosthetic sockets, the transfemoral one should be a total contact receptacle to distribute load over the maximum area, thereby reducing pressure.
Two types
1) quadrilateral socket (traditional type)
2) ischial containment socket ( its wall cover the ischial tuberosity & part of the ischiopubic ramus to augment socket stability

## Slide 14: Quadrilateral flexible socket in rigid frame viewed from above

## Slide 15: Suction suspension
Suction refers to the pressure difference inside and outside the socket.
with suction suspension, internal socket pressure < external socket pressure
Ap…… causes the socket to remain on the thigh.

## Slide 16: suspension
Three means are used to suspend the transfemoral prosthesis
Total suction
Partial suction
No suction
Total suction:-
Max control of the prosthesis, without any encumbering auxiliary suspension, can be achieved only if the socks fits very snugly to give total suction.
Notes: Suction:- internal socket pressure is less than external socket pressure.

## Slide 17: Partial suction
Socket that is slightly loose may enable patial suction susp.
Pt wears one or more socks or a liner made of silicone or other synthetic material.
Auxiliary suspension aid is needed either a fabric silesian bandage or a rigid plastic or metal hip joint and pelvic band.

## Slide 18: No suction
If socket has distal hole but no valve, then there is no pressure difference between inside and outside the socket.
The client wears one or more socks and require a pelvic band.
Loose socket makes prosthesis donning easy, but hinders control of prosthesis and sitting comfort.
Another alternative is the addition of a transfemoral suspension sleeve.