## Slide 1: Detergents
Surfactants
Perform cleaning action
Purely synthetic in nature
Need of detergents:
After the 1st world war, extreme shortage of soap.
Better cleaning action than soap

## Slide 2
First synthetic detergent was the sulfated castor oil prepared by using turkey red oil.
2nd synthetic detergent was derived by using coconut oil and called lauryl sulphate.
Commercial production…. Lauryl benzene sulfonic acid
Types of detergents:
Anionic detergents
Cationic detergents
Non-ionic detergents
Amphoteric detergents

## Slide 3: Anionic Detergents:
Most commonly used detergents/ cheapest
They ionize in water to produce anions which perform cleaning action
Further two types:
Sulfated long chain alcohols
Alkyl benzene sulfonates

## Slide 4: Cationic Detergents
They are less commonly used
They generate cation in solution which perform the cleaning action
Non-ionic detergents:
Ethoxylated amines
Ethoxylated alcohols

## Slide 5: Amphoteric Surfactants:
These surfactants contain both cationic and anionic groups in the same molecules.

## Slide 6: Raw Materials of Detergents
n-alkanes, olefins, benzene……..petroleum
Benzene… fractional distillation of coal tar
Inorganic compounds such as oleum, conc. sulfuric acid, NaOH, Na3(P3O10), some additives.
Fatty alcohols are obtained by the oxidation of olefins or by the catalytic reduction of triglycerides and fatty acids.

## Slide 7: Builders
To enhance its effectiveness and to reduce its cost.
To avoid the re-deposition of soil on fiber after washing
Sodium tripolyphosphates, trisodium phosphates………. Foaming agents, chelating agents for Ca and Mg ions
Disadvantage: eutrophication
Zeolites
Nitriloacetic acid
Sodium carbonates and silicates etc are added as fillers

## Slide 8: Other Additives:
1. optical brightners
2. Bluing agents… ultramarine blue
3.Antimicrobial agents… salicylanilides
4.Perfumes

## Slide 9: Manufacturing Process:
n-alkanes + Benzene…….. Alkyl benzene
Alkyl benzene+ oleum…… alkyl benzene suphonic acid
alkyl benzene suphonic acid + NaOH….. Sodium salt of alkyl benzene suphonic acid
Sodium salt + builders + Additives…. Detergent

## Slide 10: Fatty alcohol Sulfates
Fatty alcohols + Oleum….. Fatty alcohol sulfates
Neutralization with NaOH
Addition of builders and additives

## Slide 11: Manufacturing Process:
Preparation of alkyl benzene by friedal-craft alkylation
Sulphonation and sulfation:
Temp : 50 -55c
Neutralizer:
Alkyl benzene sulfonic acid + NaOH .. Sodium salt of alkyl benzene sulfonic acid (detergent) + water.
.Sent for storage from few hours to days
slurry
Blending tower:
Addition of additives and builders
Thickening of slurry

## Slide 12: Granulation and Finishing:
Counter current blow of hot air
Up-lifiting of granules
Separation in cyclone
Screened
Perfumed
packing