## Slide 1: Wheat Milling
Carried out by dry milling
Steps involved in wheat milling are
  Cleaning
  Tempering and conditioning
  Roller milling
  Flour treatment
1

## Slide 2: Cleaning
Wheat arriving in mill contain foreign matter
It includes dust, dirt, seeds of other crops, straw and pieces of metals
These impurities decrease milling efficiency
Cleaning is required to increase milling efficiency
2

## Slide 3: Methods of seperating wheat impurities
Cleaning methods based upon different principles
Impurities are removed on the basis of following characteristics
  Magnetic properties
  Size and dimension
  Shape
  Specific gravity
3

## Slide 4
  Behaviour in air current
  Surface friction
  Electrostatic properties
  Colour differences
4

## Slide 5: Equipments used for cleaning
Magnetic Separator
The wheat first passes by a magnet that removes iron and steel particles
Separator
Vibrating screens remove bits of wood and straw and almost anything too big and too small to be wheat
5

## Slide 6
Aspirator
Air currents act as a kind of vacuum to remove dust and lighter impurities
De-Stoner
Using gravity, the machine separates the heavy material from the light to remove stones that may be the same size as wheat kernels
Entolitre
Revolves at 800 rpm
Break infested grains and eggs of insects
6

## Slide 7
Disc Separator
The wheat passes through a separator that identifies the size of the kernels even more closely
It rejects anything longer, shorter, more round Scourer
The scourer removes outer husks, crease dirt and any smaller impurities with an intense scouring action
Currents of air pull all the loosened material away
7

## Slide 8
Color sorter
Color sorting of seeds is common practice in rice milling industry
Seeds are separated from the bulk of grains based on differences in their color
Electronic sensors are used for this purpose
Electric field
Separation is achieved by charging particles and placing them in to an electric field
Electrostatic forces cause mechanical movement which used for separation process
8

## Slide 9: Tempering and Conditioning
Tempering
Addition of water to optimum level and allow the grain to stand for some time to equilibrate moisture contents
Objectives
  To toughen the bran
  To soften the endosperm
9

## Slide 10
There are different requirements for optimum water contents and duration
  Harder wheat require more water and time for tempering
  Softer wheat require less water and time for tempering
Hard wheat grains are tempered to moisture content of 13.5% for 16-20hrs
In case of soft wheat the optimum moisture is 15% and time is 8hrs
10

## Slide 11
How to calculate quantity of water
water req.= 100- original moisture - 1 x wt of grains
100- desired moisture
11

## Slide 12
Conditioning
Tempering in conjunction with heat treatment
Commonly used by millers
  To increase the rate of water penetration wheat
  To modify wheat physiochemical characteristics
Heat conditioning
During conditioning wet wheat is heated by direct application of steam or through radiators at< 55oc
Then wheat is dried to milling moisture
12

## Slide 13
Vacuum conditioning
Grain is conditioned at 35oc
Then temperature is reduced to 25oc within vacuum treatment stages
The pericarp is not dried out, as with conditioners heated by direct application of steam or through radiators
System is absolutely independent of climate
Milling stock characteristics can be easily adjusted to quick changes in temperature and humidity
13

## Slide 14
14

## Slide 15: Roller Milling
Gradual reduction system comprising of break roll and reduction roll systems
A pair of rolls accomplishes milling
The pair of rolls rotates in opposite direction
Difference in speed of rolls is called differential
Fast roll rotates 2.5 times faster than the slower
The point at which these rolls approach each other is known as nip
15

## Slide 16
Shearing and crushing of grain take place at this point
Break roll system
Objectives are
Tear the kernel open
Flake the bran
Produce mostly middlings
Produce a minimum flour
4-5 pairs of rolls
Surfaces of rolls are corrugated
16

## Slide 17
After passing through pair of rolls the grain goes through sifter
If it is moving back and forth it is known as simple sifter and if moving in plenary motion then plane sifter
17

## Slide 18
18

## Slide 19
19

## Slide 20
Break Roll
20

## Slide 21
Size of sieve decreases from top to bottom
Different actions taking place in break roll system
  Sharp to sharp
  Dull to dull
  Sharp to dull
  Dull to sharp
Corrugations are 10-12 inches in first roll and 28-32 in last roll
21

## Slide 22
Slow speed roll hold the material and fast speed roll scrap the material
Sifter comprises of 12 sieves of different sizes
Top is coarser and lower is finer
Overs
Material which remain at top of sieve
Thrus
Material which passes through sieve
Sometime material is also sent to purifier
22

## Slide 23
Reduction roll system
8-16 pairs of rolls
Differential is 1.5:1
After passing through each pair of roll, material passes through sifter and purifier
Different fractions obtained in reduction system
Farina
From common wheat
Semolina
From durum wheat
23

## Slide 24
24

## Slide 25
Straight grade flour
Stream of ground flour obtained from all rolls
72% of total product
Permissible amount of ash in flour is0.4%
It is difficult to sift soft wheat flour because smaller particles interact with each other and form aggregates
  Short patent flour
45% flour of total product
Contain less bran and less fines
25

## Slide 26
Long patent flour
65% flour of total product
Cut off flour
20% flour between short patent and long patent flour
Air classification of flour
Flour is separated on basis of particle size
  1-17um higher protein than parent flour
  17-35um equal to parent flour
  >35um lower than parent flour
26

## Slide 27: ISSUES In Wheat Milling
Good quality protein for baking
  Gluten strength
  Gluten content
Milling – high yields/low ash
Variety and environment
Hard and soft wheats blended
Insects in wheat
Blending to meet flour specifications
27