## Slide 1: Media sterilization

## Slide 2: Sterilization of Culture Media:
the process of making something free from bacteria or other living microorganisms
The constituents of culture media, water and containers contribute to the contamination by vegetative cells and spores. The media must be free from contamination before use in fermentation (the chemical breakdown of a substance by bacteria, yeasts, or other microorganisms).
Sterilization of the media is most commonly achieved by applying heat and to a lesser extent by other means (physical methods, chemical treatment, and radiation).

## Slide 3: Heat sterilization
Heat is the most widely used sterilization technique. The quality and quantity of contamination (i.e., the type and load of microorganisms), composition of the media and its pH and size of the suspended particles are the important factors that influence the success of heat sterilization.
In general, vegetative cells are destroyed at lower temperature in a short time (around 60°C in 5-10 minutes).
However, destruction of spores requires higher temperature and relatively longer time (around 80°C for 15-20 minutes). Spores of Bacillus stearo thermophilus are the most heat resistant.
In fact, this organism is exploited for testing the sterility of fermentation equipment.

## Slide 4: Physical methods
The physical methods such as filtration, centrifugation, and adsorption (to ion-exchangers or activated carbon) are in use. Among these, filtration is most widely used.
Certain constituents (vitamins, blood components, antibiotics) of culture media are heat labile and therefore, are destroyed by heat sterilization.
Such components of the medium are completely dissolved (absolutely essential or else they will be removed along with microorganisms) and then subjected to filter sterilization.

## Slide 5: Batch sterilization
The culture media are subjected to sterilization at 121°C in batch volumes, in the bioreactor. Batch sterilization can be done by injecting the steam into the medium (direct method) or injecting the steam into interior coils (indirect method).
For the direct batch sterilization, the steam should be pure, and free from all chemical additives (that usually come from steam manufacturing process).

## Slide 6: disadvantages of batch sterilization
There are two disadvantages of batch sterilization:
1. Damage to culture media:
Alteration in nutrients, change in pH and discoloration of the culture media are common.
2. High energy consumption:
It takes a few hours (2-4 hrs.) for the entire contents of the bioreactor to attain the requisite temperature (i.e. 120°C).
Another 20-60 minutes for the actual process of sterilization, followed by cooling for 1-2 hours. All this process involves wastage of energy, and therefore batch sterilization is quite costly.

## Slide 7: Continuous sterilization:
Continuous sterilization is carried out at 140°C for a very short period of time ranging from 30 to 120 seconds. (This is in contrast to the batch fermentation done at 121°C for 20-60 minutes).
This is based on the principle that the time required for killing microorganisms is much shorter at higher temperature.
Continuous sterilization is carried out by directly injecting the steam or by means of heat exchangers.