## Slide 2: Objectives Overview
Differentiate between storage and memory
Describe the characteristics of internal hard disks
Describe the benefits of solid-state drives
Differentiate among various types of memory cards and USB flash drives
Identify uses of external hard disks and RAID
See Page 368
for Detailed Objectives

## Slide 3: Objectives Overview
Discuss the benefits and uses of cloud storage
Describe characteristics of and differentiate among types of optical discs
Explain types of enterprise storage
Identify uses of magnetic stripe cards, smart cards, RFID tags, and NFC tags
See Page 368
for Detailed Objectives

## Slide 4: Storage
A storage medium is the physical material on which a computer keeps data, information, programs, and applications
Cloud storage keeps information on servers on the Internet, and the actual media on which the files are stored are transparent to the user
Page 368

## Slide 5: Storage
A storage device is the hardware that records and/or retrieves items to and from storage media
Page 368
Reading is the process of transferring items from a storage medium into memory
Writing is the process of transferring items from memory to a storage medium

## Slide 6: Storage
Page 369
Figure 8-1

## Slide 7: Storage
Capacity is the number of bytes a storage medium can hold
Page 370
Table 8-1

## Slide 8: Storage
Items on a storage medium remain intact even when you turn off a computer or mobile device
Pages 370 - 371
Figure 8-2

## Slide 9: Storage
Access time measures:
  The amount of time it takes a storage device to locate an item on a storage medium
  The time required to deliver an item from memory to the processor
Page 371
Figure 8-3

## Slide 10: Hard Drives
A hard disk, also called a hard disk drive (HDD) contains one or more inflexible, circular platters that use magnetic particles to store data, instructions, and information
Page 373
Figure 8-4

## Slide 11: Hard Drives
The storage capacity of hard disks varies and is determined by:
  The number of platters the hard disk contains
  Whether the disk uses longitudinal or perpendicular recording
  Density
Page 374

## Slide 12: Hard Drives
Formatting is the process of dividing the disk into tracks and sectors
Page 374
Figure 8-5

## Slide 13: Hard Drives
Characteristics of a hard disk include:
Pages 374 - 375
Tracks
Sectors
Platters
Form factor
Read/write head
Revolutions per minute

## Slide 14: Hard Drives
Page 375
Figure 8-6

## Slide 15: Hard Drives
A head crash occurs when a read/write head touches the surface of a platter
Always keep a backup of your hard disk
Page 375
Figure 8-7

## Slide 16: Hard Drives
An SSD (solid state drive) is a flash memory storage device that contains its own processor to manage its storage
An SSD (solid state drive) has several advantages over traditional (magnetic) hard disks:
Pages 376 - 378
Faster access times
Faster transfer rates
Quieter operation
More durable
Lighter weight
Less power consumption
Less heat generation
Longer life
Defragmentation not required

## Slide 17: Hard Drives
Pages 378 - 379
Figure 8-9
An external hard disk is a separate freestanding storage device that connects with a cable to a USB port or other port on a computer or mobile device

## Slide 18: Hard Drives
RAID (redundant array of independent disks) is a group of two or more integrated hard disks or SSDs
Page 380
Figure 8-10

## Slide 19: Portable Flash Memory Storage
A memory card is a removable flash memory storage device that you insert and remove from a slot in a computer, mobile device, or card reader/writer
Page 381
SDHC
SDXC
miniSD
microSDHC
microSDXC
xD Picture Card
Memory Stick PRO Duo
M2
CF

## Slide 20: Portable Flash Memory Storage
Page 381
Figure 8-11

## Slide 21: Portable Flash Memory Storage
Page 382
Figure 8-12

## Slide 22: Portable Flash Memory Storage
USB flash drives plug into a USB port on a computer or mobile device
Pages 382 - 383
Figure 8-13

## Slide 23: Cloud Storage
Cloud storage is an Internet service that provides storage to computer or mobile device users
Pages 383 - 384

## Slide 24: Optical Discs
An optical disc consists of a flat, round, portable disc made of metal, plastic, and lacquer that is written and read by a laser
Page 386
Figure 8-14

## Slide 25: Optical Discs
Page 386
Figure 8-15

## Slide 26: Optical Discs
Optical discs commonly store items in a single track that spirals from the center of the disc to the edge of the disc
Track is divided into evenly sized sectors
Page 387
Figure 8-16

## Slide 27: Optical Discs
A CD-ROM can be read from but not written to
Single-session disc
A CD-R is an optical disc on which users can write once, but not erase
A CD-RW is an erasable multisession disc
Page 388

## Slide 28: Optical Discs
A DVD-ROM is a high-capacity optical disc on which users can read but not write on or erase
A DVD-R or DVD+R are competing DVD-recordable WORM formats, on which users can write once but not erase
DVD-RW, DVD+RW, and DVD+RAM are competing DVD-rewritable formats that users can write on multiple times
Page 388

## Slide 29: Enterprise Storage
Enterprise hardware allows large organizations to manage and store data and information using devices intended for heavy use, maximum efficiency, and maximum availability
  RAID duplicates data, instructions, and information to improve data reliability
Pages 389 – 390
Figure 8-18

## Slide 30: Enterprise Storage
Network attached storage (NAS) is a server that is placed on a network with the sole purpose of providing storage to users, computers, and devices attached to the network
Pages 390 – 391
Figure 8-19

## Slide 31: Enterprise Storage
A storage area network (SAN) is a high-speed network with the sole purpose of providing storage to other attached servers
Page 391
Figure 8-20

## Slide 32: Enterprise Storage
Tape is a magnetically coated ribbon of plastic capable of storing large amounts of data and information
A tape drive reads and writes data and information on a magnetic tape
Page 392
Figure 8-21

## Slide 33: Other Types of Storage
A magnetic stripe card has a magnetic stripe that contains information
A smart card stores data on an integrated circuit embedded in the card
Page 393
Figures 8-22 – 8-23

## Slide 34: Other Types of Storage
The RFID tag consists of an antenna and a memory chip that contains the information to be transmitted via radio waves
An RFID reader reads the radio signal and transfers the information to a computer or computing device
Page 394
Figure 8-24

## Slide 35: Other Types of Storage
An NFC-enabled device contains an NFC chip
An NFC tag contains a chip and an antenna that contains information to be transmitted
Most NFC tags are self-adhesive
Page 395
Figure 8-25

## Slide 36: Summary
Variety of storage options
Storage capacity and storage access times
Characteristics of hard disks, SSDs, external hard drives, and RAID
Portable flash memory storage
Advantages and various uses of cloud storage
Characteristics of optical discs
Enterprise storage options
Magnetic stripe cards, smart cards, RFID tags, and NFC chips and tags
Page 397

## Slide 37
Chapter 8 Complete