## Slide 2: Objectives Overview
Differentiate among various styles of system units on desktop computers, notebook computers, and mobile devices
Identify chips, adapter cards, and other components of a motherboard
Describe the control unit and arithmetic logic unit components of a processor, and explain the four steps in a machine cycle
Identify characteristics of various personal computer processors on the market today, and describe the ways processors are cooled
Define a bit and describe how a series of bits represents data
Explain how program instructions transfer in and out of memory
See Page 209
for Detailed Objectives

## Slide 3: Objectives Overview
Differentiate among the various types of memory
Describe the purpose and types of expansion slots and adapter cards, and differentiate among slots for various removable flash memory devices
Differentiate between a port and a connector, and explain the differences among a USB port, FireWire port, Bluetooth port, SCSI port, eSATA port, IrDA port, serial port, and MIDI port
Describe the types of buses in a computer
Explain the purpose of a power supply and describe how it keeps cool
Understand how to clean a system unit on a computer or mobile device
See Page 209
for Detailed Objectives

## Slide 4: The System Unit
The system unit is a case that contains electronic components of the computer used to process data
Page 210
Figure 4-1

## Slide 5: The System Unit
The inside of the system unit on a desktop personal computer includes:
Page 211
Figure 4-2
Drive bay(s)
Power supply
Sound card
Video card
Processor
Memory
Notes: A drive bay holds one or more disk drives. The power supply converts electricity from a power cord plugged in a wall outlet into a form that can be used by the computer

## Slide 6: The System Unit
The motherboard is the main circuit board of the system unit
  A computer chip contains integrated circuits
Page 212
Figure 4-3

## Slide 7: Processor
The processor, also called the central processing unit (CPU), interprets and carries out the basic instructions that operate a computer
  Contain a control unit and an arithmetic logic unit (ALU)
Page 213
Multi-core processor
Dual-core processor
Quad-core processor
Notes: A processor core, or simply core, contains the circuitry necessary to execute instructions. The operating system views each processor core as a separate processor. A multi-core processor is a single chip with two or more separate processor cores. Two common multi-core processors are dual-core and quad-core. A dual-core processor is a chip that contains two separate processor cores. Similarly, a quad-core processor is a chip with four separate processor cores.

## Slide 8: Processor
Page 213
Figure 4-4

## Slide 9: Processor
The control unit is the component of the processor that directs and coordinates most of the operations in the computer(control the management of a computer)
The arithmetic logic unit (ALU) performs arithmetic, comparison, and other operations
Page 214

## Slide 10: Processor
The processor contains registers, that temporarily hold data and instructions
The system clock controls the timing of all computer operations
The pace of the system clock is called the clock speed, and is measured in gigahertz (GHz)
Page 216

## Slide 11: Processor
A processor chip generates heat that could cause the chip to burn up
Require additional cooling
  Heat sinks
  Liquid cooling technology
Pages 219 - 220
Figures 4-9 – 4-10

## Slide 12: Processor
Parallel processing uses multiple processors simultaneously to execute a single program or task
  Massively parallel processing involves hundreds or thousands of processors
Page 220
Figure 4-11

## Slide 13: Data Representation
ASCII (American Standard Code for Information Interchange) is the most widely used coding scheme to represent data
Page 221
Figure 4-14

## Slide 14: Memory
Memory consists of electronic components that store instructions waiting to be executed by the processor, data needed by those instructions, and the results of processing the data
Stores three basic categories of items:
Page 223
The operating system and other system software
Application programs
Data being processed and the resulting information

## Slide 15: Memory
Each location in memory has an address
Memory size is measured in kilobytes (KB or K), megabytes (MB), gigabytes (GB), or terabytes (TB)
Page 223
Figure 4-17

## Slide 16: Memory
The system unit contains two types of memory:
Pages 223 - 224
Volatile memory
Nonvolatile memory
Loses its contents when power is turned off
Does not lose contents when power is removed
Example includes RAM
Examples include ROM, flash memory, and CMOS

## Slide 17: Memory
Page 224
Figure 4-18

## Slide 18: Memory
RAM chips usually reside on a memory module and are inserted into memory slots
Page 225
Figure 4-20

## Slide 19: Memory
Memory cache speeds the processes of the computer because it stores frequently used instructions and data
Page 227
Figure 4-22

## Slide 20: Memory
Read-only memory (ROM) refers to memory chips storing permanent data and instructions
Firmware
A PROM (programmable read-only memory) chip is a blank ROM chip that can be written to permanently
EEPROM can be erased
Page 228

## Slide 21: Expansion Slots and Adapter Cards
An expansion slot is a socket on the motherboard that can hold an adapter card
An adapter card enhances functions of a component of the system unit and/or provides connections to peripherals
  Sound card and video card
Page 230
Figure 4-26

## Slide 22: Ports and Connectors
A port is the point at which a peripheral attaches to or communicates with a system unit (sometimes referred to as a jack)
A connector joins a cable to a port
Page 232

## Slide 23: Ports and Connectors
Page 232
Figure 4-29

## Slide 24: Ports and Connectors
On a notebook computer, the ports are on the back, front, and/or sides
Pages 232 - 233
Figure 4-30

## Slide 25: Ports and Connectors
Page 233
Figure 4-31

## Slide 26: Ports and Connectors
A USB port can connect up to 127 different peripherals together with a single connector
  You can attach multiple peripherals using a single USB port with a USB hub
Page 234
Figure 4-32

## Slide 27: Ports and Connectors
Other types of ports include:
Pages 234 - 236
Firewire port
Bluetooth port
SCSI port
eSATA port
IrDA port
Serial port
MIDI port

## Slide 28: Ports and Connectors
A Bluetooth wireless port adapter converts a USB port into a Bluetooth port
A smart phone might
communicate with a notebook computer using an IrDA port
Page 235
Figures 4-33 – 4-34

## Slide 29: Ports and Connectors
A port replicator is an external device that provides connections to peripherals through ports built into the device
A docking station is an external device that attaches to a mobile computer or device
Page 236
Figure 4-35

## Slide 30: Buses
A bus allows the various devices both inside and attached to the system unit to communicate with each other
  Data bus
  Address bus
Word size is the number of bits the processor can interpret and execute at a given time
Page 237
Figure 4-36

## Slide 31: Buses
Expansion slots connect to expansion buses
Common types of expansion buses include:
Page 238
PCI bus
PCI Express bus
Accelerated Graphics Port
USB and FireWire bus
PC Card bus

## Slide 32: Bays
A bay is an opening inside the system unit in which you can install additional equipment
  A drive bay typically holds disk drives
Page 238
Figure 4-37

## Slide 33: Power Supply
The power supply converts the wall outlet AC power into DC power
Some external peripherals have an AC adapter, which is an external power supply
Page 239

## Slide 34: Putting It All Together
Home
Intel Core i5 or Intel Core 2 i3 or AMD Athlon II or AMD Sempron
Minimum RAM: 2 GB
Small Office/ Home Office
Intel Core i7 or Intel Core i7 Extreme or AMD Phenom II or AMD Athlon II
Minimum RAM: 4 GB
Mobile
Intel Core i7 Extreme or Intel Core i7 or AMD Phenom II or AMD Turion II
Minimum RAM: 2 GB
Page 239
Figure 4-38

## Slide 35: Putting It All Together
Power
Intel Xeon or Intel Itanium or AMD Opteron
Minimum RAM: 8 GB
Enterprise
Intel Core i7 or Intel Core i7 Extreme or AMD Phenom II or AMD Athlon II
Minimum RAM: 4 GB
Page 239
Figure 4-38

## Slide 36: Keeping Your Computer or Mobile Device Clean
Clean your computer or mobile device once or twice a year
Turn off and unplug your computer or mobile device before cleaning it
Use compressed air to blow away dust
Use an antistatic wipe to clean the exterior of the case and a cleaning solution and soft cloth to clean the screen
Page 240

## Slide 37: Video: The Leopard with a Time Machine
CLICK TO START

## Slide 38: Summary
Components of the system unit
How memory stores data, instructions, and information
Sequence of operations that occur when a computer executes an instruction
Comparison of various personal computer processors on the market today
How to clean the exterior and interior of a system unit
Page 241

## Slide 39
Chapter 4 Complete