## Slide 2: Objectives Overview
Describe the types of output
Explain the characteristics of various display devices
Describe the factors that affect the quality of an LCD monitor or LCD screen
Describe various ways to print
Differentiate between a nonimpact printer and an impact printer
See Page 303
for Detailed Objectives

## Slide 3: Objectives Overview
Summarize the characteristics of ink-jet printers, photo printers, laser printers, multifunction peripherals, thermal printers, mobile printers, label and postage printers, and plotters and large-format printers
Describe the uses and characteristics of speakers, headphones, and earbuds
Identify the purpose and features of data projectors, interactive whiteboards, and force-feedback game controllers and tactile output
Identify output options for physically challenged users
See Page 303
for Detailed Objectives

## Slide 4: What Is Output?
Output is data that has been processed into a useful form
Pages 304 – 305
Figure 6-1

## Slide 5: What Is Output?
An output device is any type of hardware component that conveys information to one or more people
Page 305
Display devices
Printers
Speakers, headphones, and earbuds
Data projectors
Interactive whiteboards
Force-feedback game controllers
Tactile output

## Slide 6: Display Devices
A display device visually conveys text, graphics, and video information
A monitor is packaged as a separate peripheral
  LCD monitor
  Widescreen
Pages 306 – 207
Figures 6-2 – 6-3

## Slide 7: Display Devices
Liquid crystal display (LCD) uses a liquid compound to present information on a display device
Page 308
Active-matrix display
Passive-matrix display

## Slide 8: Display Devices
The quality of an LCD monitor or LCD screen depends primarily on:
Pages 308 - 310
Resolution
Response time
Brightness
Dot pitch
Contrast ratio

## Slide 9: Display Devices
Resolution is the number of horizontal and vertical pixels in a display device
  A higher resolution uses a greater number of pixels
Pages 308 – 309
Figure 6-5

## Slide 10: Display Devices
The graphics processing unit (GPU) controls the manipulation and display of graphics on a display device
LCD monitors use a digital signal and should plug into a DVI port, an HDMI port, or a DisplayPort
Page 310
Figure 6-6

## Slide 11: Display Devices
Plasma monitors are display devices that use gas plasma technology and offer screen sizes up to 150 inches
Page 311
Figure 6-8

## Slide 12: Display Devices
Televisions also are a good output device
  Require a converter if you are connecting your computer to an analog television
Digital television (DTV) offers a crisper, higher-quality output
HDTV is the most advanced form of digital television
Page 312
Figure 6-9

## Slide 13: Video: SID: Size Matters
CLICK TO START

## Slide 14: Display Devices
A CRT monitor is a desktop monitor that contains a cathode-ray tube
  Have a much larger footprint than do LCD monitors
Page 313
Figure 6-10

## Slide 15: Printers
A printer produces text and graphics on a physical medium
  Printed information is called a hard copy, or printout
  Landscape or portrait orientation
Page 313
Figure 6-11

## Slide 16: Printers
Page 314
Figure 6-12
Before purchasing a printer, ask yourself a series of questions:

## Slide 17: Printers
Page 315
Figure 6-13

## Slide 18: Printers
A nonimpact printer forms characters and graphics on a piece of paper without actually striking the paper
Page 315
Ink-jet printers
Photo printers
Laser printers
Thermal printers
Mobile printers
Label and postage printers
Plotters
Large-format printers
Notes: 8 type of printer

## Slide 19: Printers
An ink-jet printer forms characters and graphics by spraying tiny drops of liquid ink onto a piece of paper
  Color or black-and-white
  Printers with a higher dpi (dots per inch) produce a higher quality output
Pages 316 – 317
Figure 6-15

## Slide 20: Printers
Page 317
Figure 6-16

## Slide 21: Printers
A photo printer produces color photo-lab-quality pictures
Most use ink-jet technology
PictBridge allows you to print photos directly from a digital camera
Print from a memory card and preview photos on a built-in LCD screen
Page 318

## Slide 22: Printers
Page 318
Figure 6-17

## Slide 23: Printers
Laser printer
High-speed
High-quality
Color
Black-and-white
Pages 319 - 320

## Slide 24: Printers
Page 320
Figure 6-19

## Slide 25: Printers
A multifunction peripheral (MFP) is a single device that prints, scans, copies, and in some cases, faxes
  Sometimes called an all-in-one device
Pages 320 – 321
Figure 6-20

## Slide 26: Printers
A thermal printer generates images by pushing electrically heated pins against the heat-sensitive paper
Page 321
Figure 6-21
Thermal wax-transfer printer
Dye-sublimation printer

## Slide 27: Printers
A mobile printer is a small, lightweight, battery-powered printer that allows a mobile user to print from a notebook computer, smart phone, or other mobile device
Page 321
Figure 6-22

## Slide 28: Printers
A label printer is a small printer that prints on adhesive-type material
A postage printer prints postage stamps
  Postage also can be printed on other types of printers
Page 322
Figure 6-23

## Slide 29: Printers
Plotters are used to produce high-quality drawings
Large-format printers create photo-realistic quality color prints on a larger scale
Page 322
Figure 6-24

## Slide 30: Printers
Impact printers form characters and graphics on a piece of paper by striking a mechanism against an inked ribbon that physically contacts the paper
Pages 322 - 323
Dot-matrix printer
Line printer

## Slide 31: Printers
A dot-matrix printer produces printed images when tiny wire pins on a print head mechanism strike an inked ribbon
A line printer prints an entire line at a time
Page 323
Figure 6-25

## Slide 32: Speakers, Headphones, and Earbuds
An audio output device produces music, speech, or other sounds
Page 323
Figure 6-26
Most computer users attach speakers to their computers to:
Generate higher-quality sounds for playing games
Interact with multimedia presentations
Listen to music
View movies

## Slide 33: Speakers, Headphones, and Earbuds
Headphones are speakers that cover or are placed outside of the ear
Earbuds (also called earphones) rest inside the ear canal
Page 324
Figure 6-27

## Slide 34: Speakers, Headphones, and Earbuds
Some speakers are specifically designed to play audio from a portable media player
  Wireless speakers
Page 324
Figure 6-28

## Slide 35: Speakers, Headphones, and Earbuds
Voice output occurs when you hear a person’s voice or when the computer talks to you through the speakers
Some Web sites dedicate themselves to providing voice output
Often works with voice input
VoIP uses voice output and voice input
Page 325

## Slide 36: Other Output Devices
Other output devices are available for specific uses and applications
Page 325
Data projectors
Interactive whiteboards
Force-feedback game controllers
Tactile output

## Slide 37: Other Output Devices
A data projector is a device that takes the text and images displaying on a computer screen and projects them on a larger screen
  LCD projector
  Digital light processing (DLP) projector
Pages 325 - 326
Figure 6-29

## Slide 38: Other Output Devices
An interactive whiteboard is a touch-sensitive device, resembling a dry-erase board, that displays the image on a connected computer screen
Page 326
Figure 6-30

## Slide 39: Other Output Devices
Force-feedback sends resistance to the device in response to actions of the user
Tactile output provides the user with a physical response from the device
Pages 326 – 327
Figure 6-31

## Slide 40: Putting It All Together
Page 327
Figure 6-32

## Slide 41: Putting It All Together
Page 327
Figure 6-32

## Slide 42: Putting It All Together
Page 327
Figure 6-32

## Slide 43: Output Devices for Physically Challenged Users
Many accessibility options exist for users with various disabilities
Pages 328 - 329
Figures 6-33 – 6-34

## Slide 44: Summary
Various methods of output
Several commonly used output devices
Display devices, printers, speakers, headphones, earbuds, data projectors, interactive whiteboards, force-feedback game controllers, and tactile output
Page 329

## Slide 45
Chapter 6 Complete