## Slide 1: networkTopologies
By
Rashid Naeem Khan

## Slide 2: What is networkTopologies
A networkk can be configured or arranged in different ways.
The physical layout or arrangement of connected devices in a network is called Topology.
It is the shape of a network.
Different network topologies are as under:-
  Bus Topology
  Ring Topology
  Star Topology
  Tree Topology
  Mesh Topology

## Slide 3: Bus Topology
It is simples type of network.
It supports a small number of computers.
In it, all computers or network nodes are connected to a common communication medium.
This medium is often a central wire known as bus.
The terminators are used at the end of a bus to absorb signals.
A collision can occur in bus topology if two computer.
The sending computer sends the data and destination address through the bus.
The data and address move form one computer to other in this network.
Each computer checks the address if it matches with address of cmputer, the computer keeps the data otherwise data moves to the next computer

## Slide 4: Star Topology
All computers in star topology are connected with central device called Hub.
Star topology is mostly used in client server networks.
The sending computer sends the data to the hub
The hub sends data to the receiving computer.
Each computer in star network communicates with a central hub.

## Slide 5: Ring Topology
  In this topology, each computer is connected to the next computer with the last one connected to the first.
  Thus a ring of computer is formed.
  Every computer is connected to the next computer in a ring.
  Each computer receives the message from the previous computer and transmits it to the next computer.
  The message flows in one direction.
  The message is passed around the ring until it reaches the correct destination computer.

## Slide 6: Tree Topology
A tree topology combines the characteristics of bus and star topologies.
It consists of different groups of computers attached in star topology.
The groups are then connected to a bus backbone cable.
Tree topology is used for the expansion of an existing network.

## Slide 7: Mesh Topology
In this topology, every device in the network is physically connected to every other device in the network.
A message can be sent on different possible paths from source to destination.
In it provides improved performance and reliability.
This networks are not used much in local area networks.
It is mosltly used in wide area networks.