## Slide 2: WHAT IS COLUMN?
 Column is a vertical structural member. It transmits the load from ceiling/roof slab and beam, including its self-weight to the foundation. Columns may be subjected to a pure compressive load. R.C.C. columns are the most widely used now-a-days.

## Slide 3: Columns
Columns carry primary Axial Loads and therefore are designed for compression.
Additional loads from snow, wind or other horizontal forces can cause bending in the columns.
Columns then need to be designed for Axial Load and Bending.

## Slide 4: Column
Longitudinal rebar runs vertically and is held in place by ties
Longitudinal bars are typically about 4% of the gross column area; ties are usually #3 or #4 bars
Typically designed for compression, but must be able to resist bending
Photo courtesy of John Gambatese

## Slide 5: Types Of Columns
Long Columns
Short (Strut) Columns
Intermediate Columns

## Slide 6: Long Column
When the ratio of effective length to the least radius of
gyration is greater than 45, then it is called a long column.
A long column is subjected to bending moment in addition to direct compressive stress.
The load carrying capacity of a long column is less than a short column
The load carrying capacity of a long column depends upon slenderness ratio (slenderness ratio increases then the capacity of the column decreases)

## Slide 7
LONG COLUMN :
When length of column is more as compared to its c/s dimension, it is called long column.
Long Column Le/rmin > 45
Where,
Le = effective length of column
rmin = Minimum radius of gyration

## Slide 8
Real world example:
 Here in picture we can see long columns on front of building in “The White house” Washington D.C(USA).

## Slide 9: Short Column:
 When the ratio of effective length to the least lateral dimensions of the column is less than 12, then it is called a short column.
(or)
When the ratio of effective length to the least radius of gyration is less than 45, then it is called a short column

## Slide 10: SHORT COLUMN :
 When length of column is less as compared to its c/s dimension, it is called Short column.
Short Column Le/rmin <45
Or,
Le/d < 12
 Crushing Load : The load at which short column fails by crushing is called crushing load.

## Slide 11: INTERMEDIATE COLUMN:
 Column is intermediate when 4d < L < 30d
and
30 < Le /r min < 45 or Critical slenderness ratio.

## Slide 12: What is the definition of the slenderness ratio of a column?
Slenderness ratio is the ratio of the length of a column and the least radius of gyration of its cross section
Often denoted by lambda
λ = Le/rmin

## Slide 13: Uses of slenderness ratio
It is used extensively for finding out the design load as well as in classifying various columns in short/intermediate/long
Example-
Short Steel column - lambda is less than 45. Intermediate - 30 - 45
Long - 45 above.

## Slide 14: Why this is important?
 Long columns under compression can fail via both buckling (bending side ways) as well as crushing.
Various formulas to calculate such failure characteristics extensively use the use of this ratio.

## Slide 15: Radius of gyration
Radius of gyration is used to describe the distribution of cross sectional area in a column around
its censorial axis. The radius of gyration is given by the following formula.
R.g= (I/A)^0.5
Where I is the second moment of inertia. and A is the total cross-sectional area.

## Slide 16: Calculating the radius of gyration
To calculate the radius of gyration for the cross-section of the beam in the diagram, start with the values of I that were calculated earlier.
 Ixx = 33.3 x 106 mm4
 Iyy = 2.08 x 106 mm4
Refer to the diagram for the values of b and d that are used in the calculation of A.
A = Area of cross-section = 50 mm x 200 mm = 10,000 mm2
Substitute I and A into the formula for r to give:
This is the value of the radius of gyration about the x-x axis.

## Slide 22: Failure Modes of COLUMN
Column may fail in one of three condition
Compression failure of concrete or steel reinforcement
Buckling
Combination of buckling and compression failure
Compression failure is likely to occur with columns which are short and stocky.
Buckling is probable with column which are long and slender

## Slide 23: Failure modes of columns
Compression failure
Buckling

## Slide 26: CRIPPLING LOAD OR BUCKLING LOAD
The load at which, long column starts buckling(bending) is
called buckling load or crippling load.
Buckling of column depends upon the following factors.
  Amount of load.
  Length of column
  End condition of column
  C/s dimensions of column
  Material of column.

## Slide 27: Failure Modes
 Short Columns – fail by crushing
(“compression blocks or piers” Engel)
fc = Actual compressive stress
A = Cross-sectional area of column (in2)
P = Load on the column
Fc = Allowable compressive stress per codes
Intermediate Columns – crush and buckle
(“columns” Engel)
Long Columns – fail by buckling
(“long columns” Engel)
E = Modulus of elasticity of the column material
K = Stiffness (curvature mode) factor
L = Column length between pinned ends (in.)
r = radius of gyration = (I/A)1/2
c c
A
f  P  F
 r 
 
 KL 
fcr 
2  Fcr
 2 E

## Slide 28: Find the Effective length
1. Both ends pinned
Effective length = actual length x 1.0
2. Both ends fixed
Effective length = actual length x 0.5
3. One end pinned other end fixed
Effective length = actual length x 0.7
4. One end fixed other end completely free
Effective length = actual length x 2.0

## Slide 29: (L e) for different support conditions.