## Slide 1: Introduction to ICT
Data communication
Data transmission modes
Forms and types of data transmission
Computer networks
Types of computer networks
Network architecture
Wireless networks

## Slide 2: Data communication
Data communication is a process of transferring data electronically from one place to another.
Basic elements of data communication are
  Sending device
  Receiving device
  Communication device
  Transmission medium

## Slide 3: Data communication
Sending device is a device that sends message, it is also called source or transmitter. It can be a computer, fax machine, mobile phone etc.
Receiving device is a device that receives message, it is also called sink. It can be a computer, fax machine, mobile phone etc.

## Slide 4: Data communication
Communication devices are used to transmit messages between sending and receiving devices through communication medium. Most commonly used communication devices are modem and network card.
Transmission medium is used to carry messages from one place to another, it is also called communication channel. Transmission medium can be a physical cable or wireless connection.

## Slide 5: Data Transmission Modes
Data transmission mode is the way in which data is transmitted from one place to another.
There are three data transmission modes
  Simplex mode
  Half-Duplex traffic
  Full-Duplex traffic

## Slide 6: Data Transmission Modes
In simplex mode, data can flow only in one direction, it operates in a manner similar to a one way street.
The direction of flow never changes.
A device with simplex mode can either send or receive data.
An example is a traditional television broadcast.

## Slide 7: Data Transmission Modes
In half-duplex mode, data can flow in both directions but not at the same time.
It is transmitted one way at a time.
A device with half-duplex mode can send or receive data but not at the same time resulting in a slow speed.
Internet surfing is an example of half-duplex communication.

## Slide 8: Data Transmission Modes
In Full-Duplex mode, data can travel in both directions simultaneously.
Time is not wasted in changing the direction of data flow, making it a faster way of data transmission.
An telephone is a full-duplex device.

## Slide 9: Data Transmission Modes

## Slide 10: Forms of Data Transmission
An electromagnetic or light wave used to transmit data from one place to another is called a signal.
Propagation of signals across a communication medium is called signaling.
Communication of data from one place to another in the form of signal is called transmission.

## Slide 11: Forms of Data Transmission
Two forms of data transmission are
  Digital data transmission
  Analog data transmission

## Slide 12: Forms of Data Transmission
Digital data transmission
  All data communication between the computers is in digital form.
  Digital signal is a sequence of voltage represented in binary form.
  They are in the form of electrical pulses of ON and OFF.
  Digital signals are faster and efficient and provide low error rates.

## Slide 13: Forms of Data Transmission
Analog data transmission
  Analog signal is a continuous electrical signal in the form of a wave known as carrier wave.
  Telephone line is most commonly used media for analog transmission of data.
  Light, sound and microwave are some other examples.

## Slide 14: Types of data transmission
Two types of data transmission are
  Asynchronous transmission
  Synchronous transmission

## Slide 15: Types of data transmission
In asynchronous transmission, data is transmitted character by character.
There are irregular gaps between characters in this transmission.
It is cheaper to implement because data is not saved before it is sent.

## Slide 16: Types of data transmission
In synchronous transmission, the saved data is transmitted block by block.
Each block may consist of many characters.
A large amount of information can be transmitted at a single time with this type of transmission.
It is much faster than asynchronous transmission because there is no gap between characters.

## Slide 17: Computer Network
A computer network consists of two or more computers that are connected together through some communication media to share information and resources.
The communication media can be a cable or a wireless connection.
Connected computers can be in the same room, same building or at distant locations.

## Slide 18: Computer Network

## Slide 19: Computer Network: Examples
Computer networks can be used in an office. Different people in the office can access common information. They can share their files and exchange mail. They can also print documents from any computer in the network.
Internet is also an example of a computer network in which millions of computers are connected through phone lines. People using this network can share information, files and talk with one another.

## Slide 20: Computer Network: Network Criteria
A network must meet a certain number of criteria. The most important criteria include performance, reliability and security.
Performance is measured in transit time and response time. Transit time is the time required for a message to travel from one device to another and response time is the time elapsed between an inquiry and the response.

## Slide 21: Computer Network: Network Criteria
Reliability of a network is measured by different factors such as accuracy of data, frequency of failure and time taken to recover from failure.
Security is the protection of data from unauthorized access and damage. It also includes the implementation of procedures for data recovery if it is lost or damaged.

## Slide 22: Computer Network: Advantages
Information and resource sharing
Money saving
Easy communication
Internet access sharing
Data security and management
Entertainment

## Slide 23: Computer Network: Disadvantages
Hardware and software setup costs
Hardware and software management costs
Undesirable sharing
Illegal or undesirable behavior
Data security concerns

## Slide 24: Types of Computer Network
Different types of computer networks are
  LAN - Local Area Network
  WAN – Wide Area Network
  PAN – Personal Area Network

## Slide 25: Types of Computer Network: LAN
LAN stands for local area network and is the most common type of network.
It covers a small area and usually connects the computers and other devices within one office or a building or group of buildings.
It is often used to share resources such as printers, hard disks and programs.
Each computer or device in the network is called a node, and these nodes are usually connected though wires.

## Slide 26: Types of Computer Network: LAN
A LAN that uses no wires is called a wireless LAN.
LAN can transmit data in a limited distance and number of computers that can be attached to the network is also limited.
LAN transmission speed is typically 10 Mbps to 1000 Mbps.
Example: In a computer lab, there are 40 computers connected through LAN. They can share software, files and data in the lab.

## Slide 27: Types of Computer Network: WAN
WAN stands for wide area network.
It covers a large area and connects computers and other devices in different cities and countries.
WAN usually consists of several LANs connected together.
Computers in a WAN are often connected through telephone lines, but they can also be connected through leased lines or satellites.

## Slide 28: Types of Computer Network: WAN
WAN is expensive than LAN and is not as fast as LAN.
Transmission rate is typically 56Kbps to 50 Mbps.
Examples:
  The network connecting the ATMs of a bank located in different cities.
  The network connecting NADRA offices in different cities of Pakistan.
  Internet connects millions of users all over the world to share information.

## Slide 29: Types of Computer Network: PAN
PAN stands for personal area network.
It is a network that connects personal devices using wired and wireless technology within range of about 30 feet.
Devices may include portable computer, smart phones, digital cameras and printers etc.
PAN enables devices to communicate and share data.

## Slide 30: Types of Computer Network: PAN
Wireless PANs are more common then wired PAN and use Bluetooth or Wi-Fi technology to connect devices.
Example: A PAN can be used
  to sync data from a hand held device to a desktop computer .
  Move data wirelessly to a printer.
  Transmit data from a smartphone to a wireless headset.

## Slide 31: LAN vs WAN

## Slide 32: Network Architecture
Network architecture is the design of computers and other devices in a network and how they communicate.
The two most common network architectures are
  Peer-to-peer (P2P)
  Client-server

## Slide 33: Network Architecture: Peer to Peer
Peer to Peer is a simple and inexpensive network and normally connects less than ten computers.
Each computer in the network stores files on its own storage devices and can share data and information of any computer in network.
The network operating system and application software are installed on all computers.
P2P networks are suitable for small businesses and home users.

## Slide 34: Network Architecture: Peer to Peer

## Slide 35: Network Architecture: Client-Server
Client-server is a network in which one or more computers work as servers and other computers work as clients.
A Server is a computer that provides services to the computers and other devices connected to the network and is also known as host computer.
It is more powerful than other computers in the network and have more memory.

## Slide 36: Network Architecture: Client-Server
Different services provided by the server are
  Control access to hardware, software and data.
  Centralized storage for software, data and information
  Processing data
  Sharing software
  Managing network traffic
Some servers are known as dedicated servers because they perform a specific task.
For example a file server is used to store and manage files, print server is used to manage printers and network server is used to manage network traffic.

## Slide 37: Network Architecture: Client-Server
A client is a computer in the network that is connected with a server to access different resources.
The client computer sends request to the server for resources.
The server computer provides the requested resource to the client computer.
Client computer is less powerful than server computer.

## Slide 38: Network Architecture: Client-Server

## Slide 39: Wireless networks
Wireless networks can be
  Fixed wireless system
  Mobile wireless system

## Slide 40: Wireless networks
Fixed wireless system provides little or no mobility of the computing equipment used in wireless networks.
The equipment remains at the same position.
For example a LAN can be setup using wireless technology to avoid the use of cables.

## Slide 41: Wireless networks
Mobile wireless system provides mobility of computing equipment used in wireless networks.
It also supports the mobility of users, so that mobile users can access information from anywhere and at any time.
The user does not need to maintain fixed position in the network.
Typical equipment used in mobile wireless systems are smart phones, personal digital assistant (PDA) and pagers with the internet access.