## Slide 1
Stress, Strain and Deformation: Axial Loading

## Slide 2: Objectives:
Learn and understand the concepts of internal forces, stresses, and strains
Learn and understand the key concept of constitutive relationship of linear materials
Know how to compute normal and shearing strains and stresses in mechanically and/or thermally loaded members (axial loading)
Know how to compute strains and stresses of members belonging to indeterminate structures

## Slide 3: Stress & Strain: Axial Loading
Suitability of a structure or machine may depend on the deformations in the structure as well as the stresses induced under loading. Statics analyses alone are not sufficient.
Considering structures as deformable allows determination of member forces and reactions which are statically indeterminate.
Determination of the stress distribution within a member also requires consideration of deformations in the member.
This chapter is concerned with deformation of a structural member under axial loading.

## Slide 4: Shearing Stress
A
 P
 ave
Forces P and P’ are applied transversely to the member AB.
Corresponding internal forces act in the plane of section
C and are called shearing forces.
The resultant of the internal shear force distribution is defined as the shear of the section and is equal to the load P.
The corresponding average shear stress is,
Shear stress distribution varies from zero at the member surfaces to maximum values that may be much larger than the average value.
The shear stress distribution cannot be assumed to be uniform.

## Slide 5: Shearing Stress Examples
P F
ave  A  A
Single Shear
Double Shear
A 2 A
ave  P  F

## Slide 6: Bearing Stress in Connections
A t d
 b  P  P
Bolts, rivets, and pins create stresses on the points of contact or bearing surfaces of the members they connect.
The resultant of the force distribution on the surface is equal and opposite to the force exerted on the pin.
  Corresponding average force intensity is called the bearing stress,

## Slide 7: Displacement, Deformation, and Strain

## Slide 8: Displacement, deformation, and strain
Displacement
  A vector that represents a movement of a point in a body (due to applied loads) with respect to some reference system of axes
  Translation and/or rotation
  Shape and size of the body do not change
Deformation
  A vector that represents a movement of a point in a body (due to applied loads) relative to another body point
  The shape and size of the body change (being deformed)
  Volume may be unchanged (special cases)
Strain
  Intensity of deformation
  Objects of the same materials but different sizes demonstrate different effects when subjected to the same load
  Normal strain (): measures the change in size (elongation/contraction)
  Shearing strain (): measures the change in shape (angle formed by the sides of a body)

## Slide 9: 4-5 Stress-strain-temperature relationships (constitutive relationship)
Stress vs. strain
Thermal strain
Deformation of axially loaded members

## Slide 10: Stress vs. strain relationship
Structural analysis and design requires understanding of the system of the applied forces and the material behavior
The behavior of a material can be studied by means of mechanical testing
Stress vs. strain diagrams are often used to describe the material behavior
Stress vs. strain diagrams are supposedly/theoretically identical for the same material, but technically there is always some differences

## Slide 11: Stress-Strain Diagram: Ductile Materials

## Slide 12: Stress-Strain Diagram: Brittle Materials

## Slide 13: Elastic vs. Plastic Behavior
If the strain disappears when the stress is removed, the material is said to behave elastically.
The largest stress for which this occurs is called the elastic limit.
When the strain does not return to zero after the stress is removed, the material is said to behave plastically.

## Slide 14
Linearly Elastic region
Elastic: Strain is gone when the load is gone
Stress vs. strain is linear
  E = Young’s modulus (elastic modulus, modulus of elasticity) can be used
The Hooke’s law
  The most primitive stress vs. strain relationship
– The Hooke’s law is valid only in the elastic region
For shearing,
– use G = modulus of rigidity or shear modulus
  E
  G

## Slide 15: Poisson’s ratio
A constant stated in 1811 by Siméon D. Poisson
A material loaded in one direction will undergo strains perpendicular to the direction of the load in addition to those parallel to the load
The ratio between the two strains = Poisson’s
ratio ()
lat = lateral strain = t = tranverse strain
long = longitudinal strain = a = axial strain
Relates the G to E
 a
long
  t
   lat
The sign of strain is positive when the strain is outward
E  21  G

## Slide 16: Effect of composition
Example: high alloy content causes the steel to become ductile
Low alloy content
High alloy content
Soft, ductile
Strong, brittle

## Slide 17: Effects of temperature
High temperature causes the material to become ductile

## Slide 18: Effects of loading direction
For ductile materials, tension and compression behaviors are assumed to be the same
For brittle materials, they are different

## Slide 19: Thermal strain
When unrestrained, most engineering materials expand when heated and contract when cooled
Coefficient of thermal expansion (CTE)
   = thermal strain due to a one degree (1o) change in temperature
   is a material property (and it may depend on T)
Thermal strain
Total strain
T  T
E
T
        T


## Slide 20: Deformation of axially loaded members (linear materials)
Uniform member – single load
  L  L  PL
E EA
E = Modulus of elasticity A = cross sectional area
P = tension/compression force L = undeformed length
 = normal strain
 = normal stress
  L
E

A
  P
Constitutive relation  
Definition of strain
Definition of stress

## Slide 21: Deformation of axially loaded members
Multiple loads/sizes
n n
i i
i
E A
Pi Li
i1 i1
    

## Slide 22: Example:
Department of Mechanical E
Given:
  A is a tube
  B is a solid cylinder
Determine the total deflection
   A   B

## Slide 23: Thermal Strains and Stresses
AE
 P  PL
T   T L
  thermal expansion coef.
A temperature change results in a change in length or thermal strain. There is no stress associated with the thermal strain unless the elongation is restrained by the supports.
Treat the additional support as redundant and apply the principle of superposition.
0
AE
PL 
 T L
  T   P  0
The thermal deformation and the deformation from the redundant support must be compatible.
A
  P  E T 
  T   P  0
P   AE T 

## Slide 24: Example Problem
Solution:
The change in length resulting from the temperature change is

## Slide 25
The stress needed to resist a change in length 0f 5.95 mm is
The Internal force on the cross section of the rail will be