## Slide 1: WHAT IS A STRUCTURE?
A structure is something that will support an object or a load.
A structure must be strong enough to support its own weight and whatever load is put on it !

## Slide 2: There are three types of structure :
Mass Structures
Frame Structures
Shell structures.

## Slide 3
Mass Structures are solid structures which rely on their own weight to resist loads. A single brick is a mass structure but so is a large dam.
Mass Structures

## Slide 4: Frame Structures
Frame structures are made from many small parts (called members (struts ties etc.)), joined together. Bridges, cranes and
parts of this oil rig are some examples.

## Slide 5: Shell structures
•
Shell structures are made or assembled to make one piece. Tin cans, bottles and other food containers are examples of shell structures. Larger things such as car and aeroplane bodies are examples of more complicated shell structures. Most shell structures are made from thin sheet material (which makes them light) and most have ridges or curves moulded into them (to make them strong).

## Slide 6: Natural Structures
•
Structures are not new, nature produced the first structures long before humans were able to. A leaf is a natural structure. Its veins provide support and carry nutrients. A tree has to carry the weight of its own branches as well as resisting strong winds.

## Slide 7: Manufactured structures
A manufactured structure is quite simply a structure built by human beings.
Many of Nature's structures have been copied by humans. The shell of a snail and the body of a modern car are both shell structures designed to protect their occupants.

## Slide 8: Forces on Structures
Force – push or pull that transfers energy to an object
External force – come from outside, act upon the structure. An external force is a force placed on the structure from outside, by the wind perhaps or perhaps by someone sitting or standing on it.
Internal force – force that parts exert on each other, act within structure. Internal forces are the forces which the structure must provide within itself to resist the external forces placed upon it. If the external forces are greater than the internal forces, a structure will collapse.

## Slide 9: TYPES OF FORCES
Forces acting on Structures
Forces can be either static (stationary) or dynamic
(moving).
Static forces are usually forces caused by the weight of the structure and anything which is permanently attached to it. Static Load – changes slowly or not at all, eg: bricks in a building, twigs in nest
Dynamic forces are caused by things such as wind, waves, people, and vehicles. Dynamic forces are usually much greater than static forces and are very difficult to predict.
These are the most common reason for structural failures.
Dynamic Load – move or change, eg: car crossing bridge, oil in pipeline

## Slide 10: Forces can be internal or external
5 types of recognized forces:
compression, tension, torsion, shear & bending
1. Compression – shortens or crushes
2. Tension – stretches or pulls apart
3. Torsion – twists
4. Shear – pushes parts in opposite directions
5. Bending - stretches and squashes at the same time.

## Slide 11: Forces acting on and within Structures
External forces or loads cause internal stresses to be set up in a structure. Not all forces or loads act in the same way. Forces can bend, pull, press, or twist. Each of these types of force are given special names.
Tension : Is the name given to a force which tries to pull something apart. A structural member in tension is called a tie. A Tie resists tensile stress. Tension forces stretch a material by pulling its ends apart Tensile strength measures the largest tension force the material can withstand before failing.
Compression : Is the name given to a force which tries to squash something together. A structural member in compression is called a strut. A strut resists compressive stress.. Compression forces crush a material by squeezing it together. Compressive strength measures the largest compression force the material can withstand before it loses its shape or fails.

## Slide 12
Internal Forces Within Structures
Compression, Tension, Torsion and Shear
Shear : A shear force is created where two opposite forces try to cut tear or rip something in two. Shear forces bend or tear a material by pressing different parts in opposite directions at the same time. Shear strength measures the largest shear force the material can withstand before it rips apart.
Torsion : Is the name given to a turning or a twisting force. Torsion forces twist a material by turning the ends in opposite directions. Torsion strength measures the largest torsion force the material can withstand and still spring back into its original shape.
Bending : Bending is a word you will have met before. A structure which is subjected to bending is being stretched and squashed at the same time.

## Slide 14: THE EFFECT OF FORCES ON MATERIALS
•
•
When a material is bent, stretched or compressed but returns to its original size when the load is removed, we say it behaves in an elastic way. Elastic bands are good examples.
When a material is bent, stretched or compressed but does not return to its original size when the load is removed we say it behaves in a plastic way.
Moist clay is a good example of a 'plastic' material.
A simple experiment with a paper clip will show the difference between elastic and plastic behaviour. Up to a certain point, a paper clip will spring back into shape when you bend the end outwards and let go.
If you bend it too far, it springs back slightly but stays permanently bent. When this happens, it has been bent beyond its elastic Iimit. (see Hooke’s law for springs)

## Slide 15: MEMBERS IN A STRUCTURE
•
The different parts of a frame structure are called members. Each type of member has a different job to do in supporting the structure.
A Beam is a piece of material supported at either end.
When a beam is loaded the top is compressed and the bottom is in tension.
They are usually supported by two or more Columns.
Ideally beams should be able to span a wide gap and support a load without deflecting.

## Slide 16: Beams
•
Beams used in larger structures take many different forms, some are simply solid, some are hollow, and others have special cross-sections to provide strength and rigidity.
A cantilever is a beam which is supported at one end only.
Cantilevers are used where it is not possible to have a support at both ends (a diving board for instance).
When a cantilever is loaded, the top surface is in tension and the bottom is in compression.

## Slide 17: Frame structures
Frame structures achieve most of their strength and rigidity from the way they are assembled.
Most frameworks are built using a combination of struts and ties to make triangles. Triangles make very strong and rigid structures.
Using triangles in this way is called Triangulation.

## Slide 18: Shell structures
Most shell structures achieve their strength and rigidity from the way they are shaped. Shell structures very rarely have large flat surfaces they tend to be designed and made with ribs to act as stiffeners.
Egg and light bulbs containers are good examples. Both eggs and light bulbs can withstand considerable static forces if they are applied carefully.

## Slide 19: Stress versus Strain
•
Mechanical Properties
Deal directly with behavior of materials under applied forces.
Properties are described by applied stress and resulting strain, or applied strain and resulting stress.
  Example: 100 lb force applied to the end of a rod results in a stress applied to the end of the rod causing it to stretch or elongate, which is measured as strain.
Strength: ability of material to resist application of load without rupture.
  Ultimate strength- maximum force per cross section area.
  Yield strength- force at yield point per cross section area.
  Other strengths include rupture strength, proportional strength, etc.
Stiffness: resistance of material to deform under load while in elastic state.
  Stiffness is usually measured by the Modulus of Elasticity (Stress/strain)
  Steel is stiff (tough to bend). Some beds are stiff, some are soft (compliant)

## Slide 20: Testing Procedures
•
•
Mechanical Testing
Properties that deal with elastic or inelastic behavior of a material under load
Primary measurements involved are load applied and effects of load application
Two classification of tests; method of loading and the condition of the specimen during the test
Primary types of tests
Tensile
Compression
Shear
Torsion
Flexure

## Slide 21: Mechanical Test Considerations
•
•
Principle factors are in three main areas
manner in which the load is applied
condition of material specimen at time of test
surrounding conditions (environment) during testing
Tests classification- load application
kind of stress induced. Single load or Multiple loads
rate at which stress is developed: static versus dynamic
number of cycles of load application: single versus fatigue
•
Primary types of loading
tension compression
shear
torsion
flexure
shear

## Slide 22: Terminology
26
Engineering Stress and Strain:
These quantities are defined relative to the original area and length of the specimen.
The engineering stress (e) at any point is defined as the ratio of the instantaneous load or force (F) and the original area (Ao).
The engineering strain (e) is defined as the ratio of the change in length (L-Lo) and the original length (Lo).

## Slide 23: Stress
Stress = Measure of force felt by material
Force is measured in Newtons (N):
Area is measured using metres squared (m²)
Therefore answer will be Newton/metres squared, denoted using N/m2 1 N/m2 = 1 Pa (same as pressure). Pa is the SI unit short for Pascals
Stress  Force
Area

## Slide 24: Stress
•
•
Stress: Intensity of the internally distributed forces or component of forces that resist a change in the form of a body.
– Tension, Compression, Shear, Torsion, Flexure
Stress calculated by force per unit area. Applied force divided by the cross sectional area of the specimen.
•
Note: 1MPa = 1 x106 Pa = 145 psi
•
Stress units
Pascals = Pa = Newtons/m2
Pounds per square inch = Psi Example
– Wire 12 in long is tied vertically. The wire has a diameter of 0.100 in and supports 100 lbs. What is the stress that is developed?
– Stress = F/A = F/r2 = 100/(3.1415927 * 0.052 )= 12,739 psi =
87.86 MPa
A
  F

## Slide 25:   P
The engineering stress is:
P is the load in lbs. Kgs. Etc. on the specimen and A0 is the original cross-sectional area near the center of the specimen.
On the other hand, the true stress is the load divided by the true area, which continues to be smaller by the tensile load.
The true stress continues to increase to the point of fracture,
while the engineering stress decreases to the point of fracture due to the increasing load and the constant cross-sectional area.
29
A0

## Slide 26: Strain
Strain = Measure of deformation
F
A
L
L
Strain  L
L

## Slide 27
Strain
•
•
Strain: Physical change in the dimensions of a specimen that results from applying a load to the test specimen.
Strain calculated by the ratio of the change in length and the original length. (Deformation)
•
•
Strain units (Dimensionless)
– When units are given they usually are in/in or mm/mm. (Change in dimension divided by original length)
% Elongation = strain x 100%
0
l
  l
l0
lF

## Slide 28:   l  l0
33
The engineering strain is:
l0
l is the gage length at a given load and l0 is the original gage length with zero load

## Slide 29: Strain
Example
Tensile Bar is 10in x 1in x 0.1in is mounted vertically in test machine. The bar supports 100 lbs. What is the strain that is developed if the bar grows to 10.2in? What is % Elongation?
  Strain = (lf - l0)/l0 = (10.2 -10)/(10) = 0.02 in/in
  Percent Elongation = 0.02 * 100 = 2%
Block is 10 cm x 1 cm x 5 cm is mounted on its side in a test machine. The block is pulled with 1000 kN on bone side. If the material elongation at yield is 1.5%, how far will it grow at yield?
  Strain = Percent Elongation /100 = 1.5%/100 = 0.015 cm /cm
  Strain = (lf - l0)/l0 = (lf -5)/(5) = 0.015 cm/cm
  Growth = 5 * 0.015 = 0.075 cm
  Final Length = 5.075 cm
10cm
10in
0.1
1 in
1 c
100 lbs

## Slide 30: Strain
•
•
•
•
Permanent set is a change in form of a specimen once the stress ends.
Axial strain is the strain that occurs in the same direction as the applied stress.
Lateral strain is the strain that occurs perpendicular to the direction of the applied stress.
Poisson’s ratio is ratio of lateral strain to axial strain.
Poisson’s ratio = lateral strain
axial strain
– Example
Axial Strain
Lateral Strain
Calculate the Poisson’s ratio of a material with lateral strain of
0.002 and an axial strain of 0.006
Poisson’s ratio = 0.002/0.006 = 0.333
Note: For most materials, Poisson’s ratio is between 0.25 and 0.5
Metals: 0.29 (304 SS) to 0.3 (1040 steel) to 0.35 (Mg)
Ceramics and Glasses: 0.19 (TiC) to 0.26 (BeO) to 0.31 (Cordierite)
Plastics: 0.35 (Acetals) to 0.41 (Nylons)

## Slide 31: Stress strain diagrams
36
Stress-strain diagrams plot stress against the corresponding strain produced.
Stress is the y-axis Strain is the x-axis
Stress-Strain Curve This stress-strain curve is produced from the tensile test.

## Slide 32: Stress Strain for Different Materials
37

## Slide 33: Modulus of Elasticity
38
The slope of the stress-strain curve in the elastic deformation region is the modulus of elasticity, is known as Young's modulus

E  

## Slide 34: Young’s Modulus (Tension)
Y 
A
F

L
L


F
A
L
L
Measure of stiffness
Tensile refers to tension
tensile stress
tensile strain

## Slide 35: Shear Modulus
F A
h
S  x

Sheer Stress
Sheer Strain

## Slide 36
42

## Slide 37: Bulk Modulus
F
A
B   V
V
Change in Pressure
Volume Strain

## Slide 38
Factor of safety (FoS), also known as (and used interchangeably with) safety factor (SF), is a term describing the structural capacity of a system beyond the expected loads or actual loads.
Essentially, how much stronger the system is than it usually needs to be for an intended load. Safety factors are often calculated using detailed analysis because comprehensive testing is impractical on many projects, such as bridges and buildings, but the structure's ability to carry load must be determined to a reasonable accuracy.
Many systems are purposefully built much stronger than needed for normal usage to allow for emergency situations, unexpected loads, misuse, or degradation53

## Slide 39: Calculation
54
The following formula is used to calculate FOS

## Slide 40
EXAMPLE CALCULATION
1) The tensile (material) strength of a specific metal bar is 766N/mm². the maximum permissible stress (design load) is 456N/mm². calculate the FoS.
FoS = 766N/mm² = 1.68
456N/mm²
2) A column of pre-stressed concrete will be subjected to various loads and as such is required to have a permissible stress (design load) of 23N/mm², with a FoS of 3. Calculate the compressive stress (material strength) of the concrete.
FoS (3) = compressive stress
23N/mm²
Hence compressive stress = 3 x 23N/mm² = 69N/mm²
3) Steel rebars are required to have a material strength of 524N/mm², with a FoS of 3. Calculate the design load for the steel.
FoS (3) = 524N/mm²
design load
Hence design load = 524N/mm²÷ 3 = 174.7N/mm²