## Slide 1: INTRODUCTION TO SURVEYING

## Slide 2: DEFINITION OF SURVEYING
SURVEYING is the art of determining the positions of points on or near the earth’s surface by means of measurements in the three elements of space; namely distance, direction, and elevation. (Rayner and Schmidt)
SURVEYING is the art of measuring horizontal and vertical distances between objects, of measuring angles between lines, of determining the direction of lines, and of establishing points by predetermined angular and linear measurements. (Davis, Foote, Anderson and Mikhail)
SURVEYING is the art of making such measurements of the relative positions of points on the surface of the earth that, on drawing them to scale, natural and artificial features may be exhibited in their correct horizontal or vertical relationship. (Clarke)
SURVEYING is that branch of applied mathematics which teaches the art of determining the area of any portion of the earth’s surface, the length and directions of the boundary lines, the contour of the surfaces, and of accurately delineating the whole paper. (Webster)

## Slide 3
SURVEYING is the science or art of making such measurements as are necessary to determine the relative position of points above, on, or beneath the surface of the earth, or to establish such points. (Breed, Hosmer, and Bone)
SURVEYING is the science and art of determining relative positions of points above, on, or beneath the surface of the earth, or establishing such points. (Brinker and wolf)
SURVEYING the art and science of determining angular and linear measurements to establish the form, extent, and relative position of the points, lines, and areas on or near the surface of the earth or on other extraterrestrial bodies through applied mathematics and the use of specialized equipment and techniques.(Juny Pilapil LA PUTT)

## Slide 4
TWO GENERAL CLASSIFICATIONS OF SURVEYING
PLANE SURVEYING is that type of surveying in which the earth is considered to be a flat surface, and where distances and areas involved are of limited extent that the exact shape of the earth is disregarded.
GEODETIC SURVEYING are surveys of wide extent which take into account the spheroidal shape of the earth.

## Slide 5: TYPES OF SURVEYS
CADASTRAL SURVEYS are usually closed surveys which are undertaken in urban and rural locations for the purpose of determining and defining property lines and boundaries, corners, and areas. These surveys are also made to fix the boundaries of municipalities, towns, and provincial jurisdictions.
CITY SURVEYS are surveys of the areas in and near a city for the purpose of planning expansions or improvements, locating property lines, fixing reference monuments, determining the physical features and configuration of the land, and preparing maps.

## Slide 6
CONSTRUCTION SURVEYS these are surveys which are undertaken at a construction site to provide data regarding grades, reference lines, dimensions, ground configuration, and the location and elevation of structures which are of concern to engineers, architects, and builders.
FORESTRY SURVEYS a type of survey executed in connection with forest management and mensuration, and the production and conservation of forest lands.
HYDROGRAPHIC SURVEYS refer to surveying streams, lakes, reservoirs, harbors, oceans, and other bodies of water. These surveys are made to map shore lines, chart the shape of areas underlying water surfaces, and measure the flows of the stream.They are of general importance in connection with navigation, development of water supply and resources, flood control, irrigation, production of hydro-electric power, sub aqueous constructions, and recreations.

## Slide 7
INDUSTRIAL SURVEY sometimes known as optical tooling. It refers to the use of surveying techniques in ship building, construction and assembly of aircraft, layout and installation of heavy and complex machinery, and in other industries where very accurate dimensional layouts are required.
MINE SURVEYS are surveys which are performed to determine the position of all underground excavations and surface mine structures, to fix surfaces boundaries of mining claims, determine geological formations, to calculate excavated volumes, and establish lines and grades for other related mining work.

## Slide 8
PHOTOGRAMMETRIC SURVEYS a type of survey which makes use of photographs taken with specially designed cameras either from airplanes or ground stations. Measurements are obtained from the photographs which are used in conjunction with limited ground surveys.
ROUTE SURVEYS involves the determination of alignment, grades, earthwork quantities, location of natural and artificial objects in connection with the planning, design, and construction of highways, railroads, pipelines, canals, transmission lines, and other linear projects.

## Slide 9
10. TOPOGRAPHIC SURVEYS are those surveys made for determining the shape of the ground, and the location and elevation of natural and artificial features upon it. The features shown include such natural objects as hills, mountains, rivers, lakes, relief of the ground surface, etc; and works of man, such as roads, building, ports, towns, municipalities, and bridges.

## Slide 10: Units of measurements
1. LINEAR measurements which includes the length, width, thickness, depth and the distance. The units are meter cm and mm and kilometer

## Slide 11: Other related definitions
Photogrammetry – is the science of mapping out a big track of land and consists in taking overlapping photographs from an aeroplane flown at adequate altitude and interpreting such photos on stereoscopic machines for topography or fixing land boundaries.

## Slide 12
Control – is a framework or a skeleton of a survey consisting of established station whose relative positions have been established accurately and from which the details of the map are determined.
Triangulation – is the method of establishing horizontal control by selecting stations forming-well proportioned triangles. All the angles of the triangles are measured by repetition. Only one side, called base line, is measured accurately, the other side are computed.

## Slide 13
Trilateration – is that method of fixing the horizontal control and consists in measuring all sides with electronic instruments, the angles are calculated.

## Slide 14: DISTANCE MEASUREMENTS
Errors in Measuring distances
1. tape not standard length
2. imperfect alignment of tape
3. tape not horizontal
4. tape not stretch straight
5. imperfections of observation
6. variations in temperature
7. variations in tension
8. effect of sag

## Slide 15: MISTAKES IN MEASURING DISTANCES
1. Adding or dropping a full tape length
2. Adding a foot, usually in measuring the fractional part of tape length at the end of the line.
3. Reading numbers incorrectly
4. recording numbers incorrectly
5. Reading wrong meter mark.

## Slide 16: TWO METHODS OF MEASURING DISTANCE
1. PACING – furnishes us a rapid means of approximately checking more precise measurements of distance. This principles involves the determination of individuals pace factor by dividing the average number of paces to the distance of the course using the tape.
p.f. = average number of paces / dist using the tape

## Slide 17: Then the determination of the unknown pace distance by multiplying the average number of paces by the pace factor.
Unknown distance = pace factor x average number of paces Example:
A. Determination of individuals pace factor for a measured distance of 50m?
Trial | Line | No. of paces
1 | A – B | 68
2 | B – A | 69
3 | A – B | 70
4 | B – A | 67
Solution :
Total number of paces = 68 + 69 + 70 + 67 = 274
Average number of paces = total no. of paces / no. of trials
= 274 / 4 = 68.50
Pace factor (p.f.) = measured dist by tape / ave. no. of paces
= 50 m / 68.5 = 0.73

## Slide 18: B. Determination of unknown distance:
Trial | Line | No. of Paces
1 | B – C | 38
2 | C – B | 39
3 | B – C | 38.50
Solution:
a) Total no. of paces = 38 + 39 + 38.5 = 115.50
Average no. of paces = 115 / 3 = 38.50
Unknown distance = p.f. x ave. no. of paces
= 0.73 x 38.50
= 28.105 m

## Slide 19
Percent of Difference = Difference between the true and computed value over the average between the two values.
Unknown distance = 28.105 m (computed value) Tape distance = 28.00 (true value)
% of Difference = .105 / 28.0525 x 100
= 3.74%
Percent of Error = Difference between the true value and computed value over the true value
%of error = 0.105 / 28 x 100 = 3.75%

## Slide 20
Exercises:
A. From the given field notes below:
Trial | Line | No. of paces
1 | A – B | 79.5
2 | B – A | 79.00
3 | A – B | 78.20
4 | B – A | 79.20
5 | A – B | 79.50
Compute:
Average no. of paces
pace factor if the measured distance is 70 m?

## Slide 21: B. Given the ff. data below:
Trial | Line | No. of paces
1 | B – C | 55.00
2 | C – B | 58.00
3 | B – C | 57.00
4 | C – B | 55.00
5 | B – C | 56.00
Compute:
Average no. of paces
unknown distance use p.f. as computed in problem A
If the measured distance between B – C is 50m, find the % of difference and error.

## Slide 22
Chaining or Taping :
is the operation of measuring horizontal or inclined distance by the use of tape.
Factors affecting the Tape ( tape correction)
a. Temperature Correction Ct = k ( T2 – T1)
where:
Ct = Correction for temperature ( added or subtracted )
k = temperature coefficient
( 0.0000116/0C , 0.00000645/0F)
T1 = temp during standardization of tape T2 = temp during actual measurements L = length of tape at temperature T1

## Slide 23
b. Pull Correction
Cp = ( P2 – P1)L / AE
where:
Cp = Correction for pull (Added of subtraction) E = modulus of elasticity
A = Cross-sectional area of tape
P2 = applied pull during actual measurements P1 = applied pull during standardization of tape L = length of tape at pull ( P1)

## Slide 24
C. Sag Correction Cs = w2 L3 / 24 P2
where:
Cs = correction for sag ( subtract always)
w = weight of the tape per unit length(kg/m) L = unsopported length of tape
P = applied pull during actual measurement

## Slide 25
Slope Correction
Cs = h2 / 2S
where
Cs = correction for slope ( always subtracted) h = difference in elevation between tape ends
s = slope/ inclined distance