## Slide 1: bioavailability

## Slide 2: BIOAVAILABILITY
COURSE TITLE BIOREMEDIATION AND BIODEGRADATION
DEPARTMENT OF BOTANY

## Slide 3: Bioavailability,
Bioavailability, in environmental and soil sciences, represents the amount of an element or compound that is accessible to an organism for uptake or adsorption across its cellular membrane

## Slide 4
In environmental and agricultural applications, bioavailability most often refers to availability of contaminants, such as organic pollutants or heavy metals, in soil systems and is also used frequently in determining potential risk of land application of sewage sludge or other inorganic/organic waste materials.

## Slide 5
Almost exclusively, plant roots and soil organisms uptake contaminants that are dissolved in water
Therefore, the bioavailable fraction is often likened to the dissolved (aqueous) fraction in these systems
Depending on its chemical properties, a contaminant may or may not be found in the aqueous phase. Organic contaminants may become sorbed or sequestered in organic matter through weak Van der Waals interactions or through hydrogen- or covalent bonding.

## Slide 6
Ionic compounds, such as heavy metals, can be precipitated into the solid phase.
Volatile compounds can be lost as aerosols to the soil atmosphere. In these forms, contaminants are relatively inaccessible to microbial or plant uptake and must dissociate and re-dissolve into the soil solution to become biological available.

## Slide 7
Bioavailability is a function of soil properties, time, environmental conditions, and plant and microbial characteristics [7]

## Slide 8: Factors affecting soil bioavailability
1- soil properties
2- time
3- environmental condition

## Slide 9: Soil properties
Soil properties, such as
pH,
ion exchange capacity,
soil organic matter content,
texture and porosity
influence bioavailability.
Because soils with higher ion exchange and organic matter content offer more opportunities for adsorption, typically they exhibit lower bioavailability

## Slide 10: time
As the contact time between the contaminant and soil increases, a decrease in bioavailability is observed, termed “ageing”, due to diffusion and sorption processes with mineral and organic fractions of soil.

## Slide 11: Environmental conditions
Environmental conditions influence bioavailability
Drought conditions result in lower soil water content
This can reduce the access of plants and organisms to dissolved contaminants but also can enhance precipitation of salts from solution.

## Slide 12: Heavy metal contaimination
Soils may become contaminated by the accumulation of heavy metals and metalloids
from industrial areas,
mine tailings,
disposal of high metal wastes,
land application of fertilizers,
sewage sludge,
coal combustion residues,
spillage of petrochemicals,

## Slide 13
Heavy metals constitute an ill-defined group of inorganic chemical hazards, and those most commonly found at contaminated sites are
lead (Pb), chromium (Cr), arsenic (As), zinc (Zn),cadmium (Cd), copper (Cu), mercury (Hg), and nickel (Ni)

## Slide 14
most metals do not undergo microbial or chemical degradation and their total concentration in soils persists for a long time after their introduction
Changes in their chemical forms (speciation) and bioavailability are, however, possible.
The presence of toxic metals in soil can severely inhibit the biodegradation of organic contaminants

## Slide 15: Method to remove heavy metal FROM SOIL
Vitrification.
The mobility of metal contaminants can be decreased by high-temperature treatment of the contaminated area that results in the formation of vitreous material During this process, the increased temperature may also volatilize and/or destroy organic contaminants or volatile metal species (such as Hg)
Most soils can be treated by vitrification, and a wide variety of inorganic and organic contaminants can be targeted

## Slide 16: Soil Washing.
. Soil washing is essentially a volume reduction/waste minimization treatment process.
During soil washing
, (i) those soil particles which host the majority of the contamination are separated from the bulk soil fractions(physical separation),
(ii) contaminants are removed from the soil by aqueous chemicals and recovered from solution on a solid substrate (chemical extraction)

## Slide 17: Phytoremediation
also known as green remediation, botanoremediation , agroremediation, or vegetative remediation,
This is in situ remediation
The idea of using metal-accumulating plants to remove heavy metals is known as phyto remediation
Plants may break down or degrade organic pollutants or remove and stabilize metal contaminants.