## Slide 1: TACHEOMETRY
Lecture # 8

## Slide 2: Tacheometry
Definition-It is the branch of angular surveying the Horizontal distances from station to the staff and the vertical distance of a point are determined from instrumental observation
Horizontal distance

## Slide 3: Vertical distance

## Slide 4: Situation where tacheometry can be used
• When obstacles like river, broken ground,streches of water, tacheometry gives speed & accuracy to work.
• In rough country where measurement of horizontal & vertical distances are difficult, inaccurate & slow.
• In locating contours & filling details in a topographic survey, this method is fast & best.

## Slide 5: Advantages of tacheometry
• Tacheometer is used where chaining is difficult such as river, vally, broken boundries, stiff slope, undulations.
• It is used in the preparation of contour maps, in which horizontal & vertical distances are required to be measured.
• It is used for the survey road, railway.
• It is also used for the hydrographic survey.
• It is used for checking distances measured by tape, chain & dumpy level.
• It is used where accuracy is not required.
• It saves time & money.

## Slide 6: Difference between theodolite and tacheometer
Theodolite
• It is used for measurement of horizontal & vertical angle.
• In theodolite survey , distances are measured by chain or tape.
• Suitable for plane & hilly area with less obstacles.
• More stations are required in theodolite survey.
Tacheometer
• It is used for measurement of horizontal & vertical distances.
• In tacheomtric survey ,direct measurement of distances are possible.
• Suitable in case obstacles like river broken ground.
• Less stations are required in tacheometric survey.

## Slide 7: Constants of Tacheometer
• Multiplying constant ie. (f/i) or m.
• Additive constant ie (f+c) or C.
Where f= focal length of image glass c= legth of image

## Slide 8: Object of tacheometry
• Preparation of contour maps or plans.
• Used in hydrographic survey.
• Location survey for roads,railways, reservoir etc.
• For checking of more precise measurements.

## Slide 9: Instrument used in Tacheometer
I) Tacheometer
II) Levelling or stadia rod
I)Tacheometer –It is a transit theodolite provided
with a stadia diaphragm.
• The diaphragm is provided with two horizontal stadia hairs in addition to regular cross hair.
• Additional hair should be equidistant from central one.
• Types of diaphragm commonly used as follows.

## Slide 10: Types of diaphragm

## Slide 11: Types of Telescope in Tacheometry
• External focusing
• Internal focusing
• External focusing fitted with anallatic lens.

## Slide 12
Anallatic lens -It is an additional lens generally provided in the external focusing tacheometer between object glass & eyepiece
Advantages of anallatic lens.
1) For calculation of horizontal & vertical distances constant (f+c)=0, if tacheometer is provided with anallatic lens.
2) Calculation becomes simple.

## Slide 13: Essential characteristics of Tacheometer
• The value of constant (f/i)=100.
• The telescope should be provided with anallatic lens.
• The telescope should be powerful, magnification should be 20 to 30 times the diameter.
• The vision through the telescope should be clear & bright image at longer distance.

## Slide 14
II)Levelling staff or stadia rod.
• Levelling staff or stadia rodused with tacheometer may be usual type of levelling staff.
• It may be folding or telescopic with is 5 cm to 15 cm. & height 3 m to 5 m.
• It may measure meter , decimeter & centimeter.

## Slide 16: Fixed Hair Method
• In this method, the distance between two stadia hair is fixed.
• The reading corresponding to three cross hair is taken and difference between top and bottom hair is found out known as staff intercept.

## Slide 17: Principle of stadia method
From similarity of triangle POQ & poq . PR/pr =OQ/oq
S/i = f1/f2
By lens formula 1/f= (1/f1)+(1/f2)
Multyplying f1 to both side f1×(1/f) = f1×(1/f1)+f1×(1/f2) f1/f = 1+(f1/f2)
Put values of (f1/f2) = S/i f1/f = 1+ (S/i )
(f1/f)-1 = S/i (f1-f)/f = S/i
f1= S/i ×f+f eq 1
Now, D= f1+d or f1=D-d eq 2 Put values of equation 2 in 1
D-d = S/i×f+f
D=(f/i)×S+(f+d) eq 3
(f/i) =multiplying constant= m (f+d)= additive constant =c D= ms+ c

## Slide 18
P, Q, R=Three line of sight on staff corresponding to three line. P, q, r=the stadia hairs
O= optical center of object glass. pr= i = stadia interval.
PR= s = staff intercept.
f = focal length of object glass.
f1 = horizontal distance between center of object glass to the staff station.
f1 = horizontal distance of diaphragm from ‘o’
D= horizontal distance of staff station from vertical axis of taceometer.
d= horizontal distance between vertical axis of tacheometer & center bof object glass.

## Slide 19: Fixed Hair Method
There are three different cases used.
Case I): Line of sight is horizontal and the staff held is vertical.
Case II): Line of sight is inclined and the staff held is vertical.
Case III): Line of sight is inclined and the staff held is normal to the line of sight.

## Slide 20: Case I): Line of sight is horizontal and the staff held is vertical.

## Slide 21: Case II): Line of sight is inclined and the staff held is vertical.
Vertical Distance V=(f/i)S Sin2θ+ (f+c) Sinθ
2
Horizontal Distance D =(f/i)S Cos2θ+ (f+c) Cosθ Where, θ is angle between horizontal line of sight & central reading

## Slide 22: Thanks