## Slide 1
Civil Engineering Department
College of Engineering and Technology(CET)
UOS
Lecture-13
Highway Surveying

## Slide 2: Highways
It gives the maximum service to one and all
It gives maximum flexibility for travel with reference to route, direction, time and speed of travel
It provide door to door service
Other modes are depend on it
It requires small investment for the government
Motor vehicles are cheaper than other carriers like rail locomotive and wagons
It saves the time for short distance
High degree of accident due to flexibility of movement

## Slide 3: Scope of highway engineering
Development, planning and location
Highway design, geometric and structure
Traffic performance and its control
Materials, construction and maintenance
Economic, finance and administration

## Slide 4: ROLE /IMPACT OF TRANSPORTATION
Economic Development
Social Development
Spatial Development
Cultural Development
Political Development

## Slide 5: Characteristics of road transport
Roads are used by various types of road vehicles, like passenger cars, buses, trucks, pedal cycle and animal drawn vehicle.
It requires a relatively small investment for the government.
It offers a complete freedom to road users to transfer the vehicle from one lane to another and from one road to another according to need and convenience.
Speed and movement is directly related with the severity of accident.
Road transport is the only means of transport that offers itself to the whole community alike.

## Slide 6: Classification of Highways
Depending on weather
All weather roads
Fair weather roads
Depending the type of Carriage way
Paved roads(WBM)
Unpaved roads(earth road or gravel road)
Depending upon the pavement surface
Surfaced roads(bituminous or cement concrete road)
Un surfaced roads

## Slide 7: Classification of Highways
Based on the Traffic Volume
Heavy
Medium
Light
Based on Load or Tonnage
Class 1 or Class 2 etc or Class A , B etc Tonnes per day
Based on location and function ( Nagpur road plan )
National highway (NH)
State highway (SH)
Major district road (MDR)
Other district road (ODR)
Village road (VR)

## Slide 8: Highway alignment and surveys

## Slide 9: Highway alignment
The position or lay out of centre line of the highway on the ground is called the alignment.
It includes straight path, horizontal deviation and curves.
Due to improper alignment , the disadvantages are,
  Increase in construction
  Increase in maintenance cost
  Increase in vehicle operation cost
  Increase in accident cost
Once the road is aligned and constructed, it is not easy to change the alignment due to increase in cost of adjoining land and construction of costly structure.

## Slide 12: Requrements of highway alignment
Short
Easy
Safe
Economical
Short- desirable to have a short alignment between two terminal stations.
Easy- easy to construct and maintain the road with minimum problem also easy for operation of vehicle.
Safe- safe enough for construction and maintenance from the view point of stability of natural hill slope, embankment and cut slope also safe for traffic operation.
Economical- total cost including initial cost, maintenance cost and vehicle operation cost should be minimum.

## Slide 13: Factors controlling alignment
Obligatory points
Traffic
Geometric design
Economics
Other considerations Additional care in hill roads
Stability
Drainage
Geometric standards of hill roads
Resisting length

## Slide 14: Factors controlling alignment cont...
Obligatory points
Obligatory points through which alignment is to pass
Examples:-bridge site, intermediate town , Mountain pass etc…
Obligatory points through which alignment should not
pass.
Examples:-religious places, costly structure, unsuitable land etc…
Traffic
origin and destination survey should be carried out in the area and the desire lines be drawn showing the trend of traffic flow.
New road to be aligned should keep in view the desired lines, traffic flow patterns and future trends.

## Slide 15: Geometric design
Design factors such as gradient ,radius of curve and sight distance also govern the final alignment of the highway.
Gradient should be flat and less than the ruling gradient or design gradient.
Avoid sudden changes in sight distance, especially near crossings
Avoid sharp horizontal curves
Avoid road intersections near bend
Economy
Alignment finalised based on total cost including initial cost, maintenance cost and vehicle operation cost.
Other consideration
Drainage consideration, political consideration
Surface water level, high flood level
Environmental consideration

## Slide 16: Topographical control points
The alignment, where possible should avoid passing through
  Marshy and low lying land with poor drainage
  Flood prone areas
  Unstable hilly features
Materials and constructional features
  Deep cutting should be avoided
  Earth work is to be balanced; quantities for filling and excavation
  Alignment should preferably be through better soil area to minimize pavement thickness
  Location may be near sources of embankment and pavement materials

## Slide 17: stability
A common problem in hilly roads is land sliding
The cutting and filling of the earth to construct the roads on hilly sides causes steepening of existing slope and affect its stability.
Drainage
Avoid the cross drainage structure
The number of cross drainage structure should be minimum.
Geometric standard of hilly road
Gradient, curve and speed
Sight distance, radius of curve
Resisting length
The total work to be done to move the loads along the route taking horizontal length, the actual difference in level between two stations and the sum of the ineffective rise and fall in excess of floating gradient. Should kept as low as possible.

## Slide 18: Engineering Surveys for Highway locations
Before a highway alignment is finalised in highway project, the engineering survey are to be carried out. The various stages of engineering surveys are
Map study (Provisional alignment Identification)
Reconnaissance survey
Preliminary survey
Final location and detailed surveys

## Slide 19: MAP STUDY
From the map alternative routes can be suggested in the office, if the topographic map of that area is available.
The probable alignment can be located on the map from the fallowing details available on the map.
  Avoiding valleys, ponds or lake
  Avoiding bend of river
  If road has to cross a row of hills, possibility of crossing through mountain pass.
Map study gives a rough guidance of the routes to be further surveyed in the field

## Slide 20: RECONNAISSANCE SURVEY
To confirm features indicated on map.
To examine the general character of the area in field for deciding the most feasible routes for detailed studies.
A survey party may inspect along the proposed alternative routes of the map in the field with very simple instrument like abney level, tangent clinometer, barometer etc…. To collect additional details.
Details to be collected from alternative routes during this
survey are,
  Valleys, ponds, lakes, marshy land, hill, permanent structure and other obstruction.
  Value of gradient, length of gradient and radius of curve.

## Slide 21: RECONNAISSANCE SURVEY cont..
Number and type of cross drainage structures.
  High Flood Level (HFL)
  Soil Characteristics.
  Geological features.
  source of construction materials- stone quarries, water sources.
Prepare a report on merits and demerits of different alternative routs.
As a result a few alternate alignments may be chosen for further study based on practical considerations observed at the site.

## Slide 22: Preliminary survey
Objective of preliminary survey are:
To survey the various alternative alignments proposed after the reconnaissance and to collect all the necessary physical information and detail of topography, drainage and soil.
To compare the different proposals in view of the requirements of the good alignment.
To estimate quantity of earthwork materials and other construction aspect and to workout the cost of the alternate proposals.
Methods of preliminary survey:
a) Conventional approach-survey party carries out surveys using the required field equipment, taking measurement, collecting topographical and other data and carrying out soil survey.

## Slide 23: Preliminary survey cont…
Longitudinal and cross sectional profile.
: 100 – 200m
: 50m
: 30m
Plain Terrain`
Rolling Terrain
Hilly Terrain
Other studies
Drainage, Hydrological survey, soil survey, Traffic and Material survey.
b) Modern rapid approach-
By Aerial survey taking the required aerial photographs for obtaining the necessary topographic and other maps including details of soil and geology.
Finalise the
best alignment from all considerations by
comparative analysis of alternative routes.

## Slide 24: Final location and detailed survey
The alignment finalised at the design office after the preliminary survey is to be first located on the field by establishing the centre line.
Location survey:
Transferring the alignment on to ground.
This is done by transit theodolite.
Major and minor control points are established on the ground and centre pegs are driven, checking the geometric design requirements.
Centre line stacks are driven at suitable intervals, say 50m interval in plane and rolling terrains and 20m in hilly terrain.

## Slide 25: Final location and detailed survey
cont..
Detailed survey:
Temporary bench marks are fixed at intervals of about 250m and at all drainage and under pass structure.
Earthwork calculations and drainage details are to be workout from the level books.
Cross sectional levels are taken at intervals of 50-100m in Plane terrain, 50-75m in Rolling terrain, 50m in built-up area, 20m in Hill terrain.
Detail soil survey is to be carried out.
CBR value of the soils along the alignment may be determined for design of pavement.
The data during detailed survey should be elaborate and complete for preparing detailed plans, design and estimates of project.

## Slide 26: Drawing and Report
Key map
Index map
Preliminary survey plans
Detailed plan and longitudinal section
Detailed cross section
Land acquisition plans
Drawings of cross drainage and other retaining structures
Drawings of road intersections
Land plans showing quarries etc

## Slide 27: New highway project
Map study
Reconnaissance survey
Preliminary survey
Location of final alignment
Detailed survey
Material survey
Geometric and structural design
Earth work
Pavement construction
Construction controls

## Slide 28: Thanks