## Slide 1: Quality Control In Feed Processing

## Slide 2: Any good feed quality-control program contains four components
Ingredient quality
Process control
Finished feed quality
Control of toxic substances, including pathogenic micro-organisms.

## Slide 3: Ingredient quality
What is quality?
Quality has been defined by various individuals as “fitness for use” or “meeting an expectation” or “degree of excellence or “conforming to a standard.”
Although near infrared spectro-photometry (NIRS) is used by a significant number of manufacturers to rapidly determine the moisture, fat, protein and fiber content of an ingredient sample, many feed manufacturers do not analyze ingredients prior to use.

## Slide 4: The following steps outline one approach to communicating your commitment to quality
Commitment to quality begins with you :
This means that you MUST NOT look for bargains in feed ingredients and that quality, NOT price must be foremost .

## Slide 5: 2. Decide what you want in ingredients and put it in writing
Visual appearance of the product, physical characteristics (e.g., grind or bulk density) of the product, expected analytical assay values, sampling procedures, analytical assay methods, criteria for refusing to accept ingredient loads and deficiency claim procedures. Discuss these specifications with your suppliers to determine whether or not they can supply your needs.

## Slide 6: 3. Examine all incoming ingredients thoroughly
It is particularly important at this point to be certain that samples of the load are collected correctly.
Following sample collection, appropriate on-site quality control tests (e.g.: moisture, test weights, mycotoxins, rancidity, etc.) should be performed.

## Slide 7: 4. Have ingredient samples analyzed by a qualified laboratory
This step is also necessary since laboratory results are necessary to provide the ultimate judgment of ingredient quality.

## Slide 8: 5. Communicate often with your suppliers about quality
Let your suppliers know that you are aware of the quality of their product. This will help your suppliers know that you really care about receiving high-quality ingredients.

## Slide 9: 6. Adjust your formulas to reflect the assays you are receiving
If you do not adjust your formulas to reflect the actual assays, you have, in effect, wasted much of the time and money you spent on the assays.

## Slide 10: Process Control
The process by which high-quality ingredients are made into high-quality feeds involves three components within the feed mill:
personnel
machinery
procedures

## Slide 11: Personal
Three general characteristics should be sought in new mill employees productivity, interest and the ability to work as a team member.

## Slide 12: Machinery
Equipment selection, operation, repair and troubleshooting can become a very complicated matter, which can not be covered adequately in a short space. However, applying the following general points to each specific piece of equipment will help reduce machinery problems:
Application: Was the equipment designed to do the job it is doing?
Installation: Was the equipment installed according to the manufacturer’s recommendations?
Adjustment: Are the critical adjustment points within the machine set correctly?
Operation: Is the machine being operated according to the manufacturer’s recommendations?
Capacity: Is the equipment being run within the rated capacity?
Lubrication: Is the correct amount of the proper lubricant used within the correct time frame in the machine?
Maintenance: Can you predict when maintenance and possible repairs will be needed on each piece of equipment?

## Slide 13: Procedure
Procedural difficulties are usually fairly easy to identify since problems will tend to repeat. However, every procedure instituted should incorporate the following:
Communication: Does the person doing the procedure understand what is expected? If another person had to take over this job would he/she understand?
Identification: Are controls on equipment clearly identified? Are bagged ingredients clearly labeled and stored in an orderly manner?
Traceability: Will this procedure allow you to trace problems to their source?
Verification: Are samples being taken and stored that will allow you to verify the source of the problem?
Records: Are all records being kept of use? If records are of no use or potential use discontinue collection. Useful records should be stored in a clean, safe and accessible place.

## Slide 14: Quality and process control
Ingredient inventories
Good ingredient inventory systems meet the following criteria:
They are simple and understood by all,
They include physical inventories,
They are accurate,
They consider history and forecasts, and
They are used.

## Slide 15: Bin cleaning
Finished feed and ingredients storage bins should be inspected at least once each month and cleaned as needed.
Entering any bin for cleaning the following precautions should be taken:
Verify that the bin is suitable for entry e.g., is it too hot?
Verify that the lock out program has been activated and notify other operators that you are entering the bin,
Be certain that a responsible, trained individual will remain with the person for the duration of his/her stay in the bin,
Verify that lighting, hoisting, safety and respiration equipment functions properly, and
Verify that first aid equipment is well supplied and ready for use

## Slide 16: Grinding
Hammer condition and wear should be checked daily.
Magnets should be cleaned and checked for correct operation daily or at the shift change.

## Slide 17: Truck inspection and cleaning
Truck drivers should be held responsible for the soundness and cleanliness of their trucks (both inside and outside).

## Slide 18: Batch system validation
Begin the validation process by verifying that a clean finished-feed bin is available. Next, batch and mix a mash formula in the usual manner and record the batch weight. Convey the batch to the clean finished-feed bin, load it out into one compartment of a bulk truck and record the truck weight. Repeat this process until four compartments have been loaded. Batch weights and truck weights should be within 1% of each other.

## Slide 19: Pelleting and Pellet Cooling
Conditioning temperature
Conditioning temperature should be as hot as possible (preferably greater than 180° F.
The heat of conditioning is important in the activation of mold inhibitors and the destruction of pathogens such as salmonella.
Cool-Pellet temperature. The temperature of adequately cooled pellets (or crumbles) will be within 10;dF of atmospheric temperature.

## Slide 20: Pelleting and Pellet Cooling
Moisture gain
Moisture gain can accelerate mold spoilage problems. While no moisture gain is a worthy goal, a more attainable goal is less than 0.5%. Moisture gain should be checked once each month.

## Slide 21: Finished Feed Quality
However, finished-feed assays are necessary and important because they provide the mill with a “final report card” on how well quality was controlled.

## Slide 22: Control pests
Stored product Insects
Lesser grain borer
Almond moth
Khapra and warehouse beetle
Foreign grain beetle
And many others pests like rats, birds, insects, rodents avoid all these pests to feed.